## Slide 1: OSPF with FRRouting
Gianluca Rizzo

## Slide 2: Summary
Intro to Link State Routing
OSPF
OSPF with FRRouting

## Slide 3: Link State Routing

## Slide 4: Least-cost path routing
Goal: find least-cost path from each source router to each destination router
Let’s see a simple algorithm for least cost path routing process
  We start from a centralized algorithm (i.e., every router has the full map of the network)
  The algorithm proceeds in steps
Notes: So, the goal of least-cost path routing is to find the least-cost path (or least-cost route) from each source router to each destination router.

## Slide 5
u
z
v
4
1
2
dest.
next hop
z
v
cost
*
Notes: It’s time to dive in and study a representative routing algorithm.
This is a centralized algorithm, in the following sense:
first, *all* routers exchange information about their adjacent links;
once each router has computed the network graph (with link costs), it runs this algorithm to compute the best path to each of the other routers.
So, each router runs its own separate instance of the algorithm. But given that they all provide the same input to the algorithm (the same network graph and link costs), they all reach compatible conclusions.
Let’s now focus on router u and see what happens when router u runs the algorithm.
The algorithm works in steps.

## Slide 6
u
z
v
4
1
2
dest.
next hop
z
v
z
v
cost
4
1
*
Notes: In the first step, the algorithm considers only the links that are directly connected to router u. It forgets about the rest of the network (it’s as if the other links do not exist).
Considering *only* these two direct links,
the algorithm fills its table as follows:
- It asks: is there a path from router u to router z?
- The answer is: yes, there exists a direct path, the next-hop is router z itself, and the cost is 4.
- Then it asks: is there a path from router u to router v?
- The answer is: yes, there exists a direct path, the next-hop is router v itself, and the cost is 1.

## Slide 7
u
z
v
4
1
2
dest.
next hop
z
v
z
v
cost
4
1
v
3
*
Notes: In the second step, the algorithm chooses a neighbor of router u — in our example, router v, and considers the links that are directly connected to that neighbor as well.
The algorithm asks: can router u improve its existing paths by routing through router v?
Let’s consider the path to destination z:
- Can router u improve its path to destination z by routing through v?
- Yes, indeed, it can.
- So, the algorithm removes the old, direct path from u to z and adds a new path through v.
- Now let’s update the table: for destination router z, the new next hop is router v, and the new cost is 3.
Now let’s consider the path to destination v:
- Can router u improve its path to destination v by routing through router v?
- No, because the path to destination v is already through router v itself, so there is nothing to improve.
At this point, the algorithm is done:
it has computed the least-cost path from router u to every other router in the network.

## Slide 8
v
2
1
3
u
z
x
2
1
dest.
next hop
z
v
cost
x
*
Another example (try it yourself)
Notes: Let’s look at a second example.
Again, we will concentrate on router u.

## Slide 9
v
2
1
3
u
z
x
2
1
dest.
next hop
z
v
cost
x
-
-
v
1
x
2
*
Notes: In the first step, the algorithm considers only the the links that are directly connected to router u.
Considering only these 2 links:
- Router u cannot reach router z yet.
- Router u can reach router v through a direct link.
- The next hop is router v itself, and the cost is 1.
- Router u can reach router x through a direct link.
- The next hop is router x itself, and the cost is 2.

## Slide 10
v
2
1
3
u
z
x
2
1
dest.
next hop
z
v
cost
x
-
-
v
1
x
2
v
4
*
Notes: In the second step, the algorithm considers router v, and the links that are directly connected to router v.
The algorithm asks: can router u improve its existing paths by routing through router v?
Let’s consider the path to destination router z:
- Can router u improve its path to destination z by routing through router v?
- Yes, it can: it previously could not reach router z at all, now it can reach router z through router v.
- So, the algorithm adds a new path through v.
- The next hop is router v, and the cost is 4.
Now let’s consider the path to destination router v:
- Can router u improve its path to destination v by routing through router v?
- No, because the path to destination router v is already through router v itself, so there is nothing to improve.
The same is true about the path to destination router x.

## Slide 11
v
2
1
3
u
z
x
2
1
dest.
next hop
z
v
cost
x
-
-
v
1
x
2
v
4
x
3
*
Notes: In the third step, the algorithm considers the other neighbor, router x,
and the links that are directly connected to router x.
The algorithm asks: can router u improve its existing paths by routing through router x?
Let’s consider the path to destination router z:
- Can router u improve its path to destination router z by routing through router x?
- Yes, it can, so the algorithm removes the old path through router v, and adds a new path through router x.
- The new next hop is router x, and the new cost is 3.
None of the other paths can be improved, so, the algorithm is done:
it has computed the least-cost path from router u to every other router in the network.

## Slide 12: Link-state routing algorithm for source u
Input: router graph & link costs
Output: least-cost path from source router u to every other router
Notes: What we saw is an example of a link-state routing algorithm:
It takes as input is the graph of all routers and the costs of all the links between them.
It produces as output the least-cost path from a given source router to every other router in the network.

## Slide 13: Link-state routing algorithm for source u
(Logically) centralized algorithm == It does not require interaction between routers in the computing phase.
  It involves a set of computing tasks that may run on a single entity, or be distributed on each router
  Routers exchange only info on which to run the algorithm (the network topology)
Option #1: Router u runs the algorithm
Option #2: A separate computer (“network controller”) runs the algorithm, and distributes results to all routers
Notes: A link-state routing algorithm is a centralized algorithm, in the sense that, given the input (network graph and link costs), the algorithm is run on a single entity.
One option is that that entity is the router itself, i.e., each router computes the least-cost path from itself to every other router in the network. This is what is typically done in most networks today.
Another option is that a separate computer, called a “network controller” runs the algorithm on behalf of all the routers, i.e., computes the least-coast path from every router to every other router in the network, and communicates the results to all the routers.

## Slide 14: The routing algorithm we have seen is Dijkstra’s Algorithm
At each step, consider a new router
  starting from “closest” neighbor
Check whether current paths can be improved
  by using that router as an intermediate point
End when no improvement is possible
Notes: The particular link-state routing algorithm that we discussed is called Dijstra’s algorithm.
In summary:
At each step, the algorithm considers a new router.
It checks whether it can improve the previously computed paths by routing through this new router.
It ends when no improvement is possible.
The next example gives you one more example of running Dijkstra’s algorithm, but without any narration.

## Slide 15
2
1
3
z
2
1
v
y
x
3
5
1
2
u
w
5
dest.
next hop
z
w
cost
y
v
x
*
Notes: And one more example.
We always concentrate on the instance of the algorithm run by router u.

## Slide 16
2
1
3
z
2
1
v
y
x
3
5
1
2
w
u
5
dest.
next hop
z
w
cost
y
v
x
-
-
v
2
x
1
w
5
-
-
*

## Slide 17
2
1
z
2
1
v
y
x
3
5
1
2
u
w
3
5
dest.
next hop
z
w
cost
y
v
x
-
-
v
2
x
1
w
5
-
-
x
4
x
2
*

## Slide 18
2
1
z
2
1
v
y
x
3
5
1
2
u
w
3
5
dest.
next hop
z
w
cost
y
v
x
-
-
v
2
x
1
w
5
-
-
x
4
x
2
*

## Slide 19
2
1
3
z
2
1
v
y
x
3
5
1
2
u
w
5
dest.
next hop
z
w
cost
y
v
x
-
-
v
2
x
1
w
5
-
-
x
4
x
2
x
4
3
*

## Slide 20
2
1
3
z
2
1
v
y
x
3
5
1
2
u
w
5
dest.
next hop
z
w
cost
y
v
x
-
-
v
2
x
1
w
5
-
-
x
4
x
2
x
3
4
*

## Slide 21
2
1
3
z
2
1
v
y
x
3
5
1
2
u
w
5
dest.
next hop
z
w
cost
y
v
x
-
-
v
2
x
1
w
5
-
-
x
4
x
2
x
3
4
*

## Slide 22: Link-state + distance-vector
They solve the same problem: compute the least-cost path from each source router to each destination router
Notes: We discussed two types of routing protocols: link state and distance vector.
They both solve the same problem: compute the least-cost paths between routers.
But, they do it…

## Slide 23: Link-state vs. distance-vector
Link state: each entity first obtains complete view of the network, then computes the least-cost paths
Distance vector: each entity obtains incrementally new information about the network at every round
Notes: differently: …
Here’s a question for you: which one is better and in what scenario? Which one do you think finishes faster? Which one requires more resources? Think about it.
Build a comparative table. Draw your conclusions.

## Slide 24: OSPF

## Slide 25: about ospf
open shortest path first
an interior gateway protocol
 | Specification | Authentication Confidentiality
version 2 | rfc 2328 | rfc 5709
version 3 (with ipv6 support) | rfc 5340 | rfc 4552

## Slide 26: ospf: overview
each router floods its local state (usable interfaces, reachable neighbors) through the network, using link state advertisements (lsa)
based on this information, each router builds and maintains a link state database (lsdb) describing the whole network topology
  identical for (almost) all routers
  each entry is a router’s local state
each router uses the lsdb to compute a shortest path tree rooted at itself
  interfaces may be assigned costs

## Slide 27: Contents
1. Link state
  flooding topology information
  finding the shortest paths (Dijkstra)
2. Hierarchical routing with areas
3. OSPF
  database modelling
  neighbor discovery - Hello protocol
  database synchronization
  link state updates
  examples

## Slide 28: 1. Link State Routing
Principle of link state routing
  each router keeps a topology database of whole network
  link state updates flooded, or multicast to all network
  routers compute their routing tables based on topology often uses Dijkstra’s shortest path algorithm
Used in OSPF (Open Shortest Path First), IS-IS (similar to OSPF)and PNNI (ATM routing protocol)

## Slide 29: (a) Topology Database Synchronization
Neighbouring nodes synchronize before starting any relationship
  Hello protocol; keep alive
  initial synchronization of database
  description of all links (no information yet)
Once synchronized, a node accepts link state advertisements (LSA)
  contain a sequence number, stored with record in the database
  only messages with new sequence number are accepted
  accepted messages are flooded to all neighbours
  sequence number prevents anomalies (loops or blackholes)

## Slide 30: Example network
n1
A
B
n6
D
E
n4
n3
C
n5
n2
F
n7
Each router knows directly connected networks

## Slide 31: Initial routing tables
net type
n1 Ether
n2 P-to-P
A
n1
A
B
n6
D
E
n4
n3
C
n5
n2
F
n7
net type
n6 Ether
n5 P-to-P
D
net type
n6 Ether
n7 Ether
E
net type
n1 Ether
n7 Ether
F
net type
n1 Ether
n4 P-to-P
n5 P-to-P
C
net type
n3 Ether
n2 P-to-P
n4 P-to-P
B
Notes: OSPF: type of link (Bcast, NBMA, P-to-P), plus the metric of each link

## Slide 32: After Flooding
rtr net cost
A n1 10
A n2 100
B n3 10
B n2 100
B n4 100
C n1 10
C n4 100
C n5 100
D n6 10
D n5 100
E n6 10
E n7 10
F n1 10
F n7 10
The local metric information is flooded to all routers
After convergence, all routers have the same information
n1
A
B
n6
D
E
n4
n3
C
n5
n2
F
n7

## Slide 33: (b) Topology graph
Arrows routers-to-nets with a given metric
  except P-to-P, stub, and external networks
From nets to routers, metric = 0
A
B
C
D
F
E
100
10
10
10
10
100
100
n1
100
n6
n7
n3
100
10
100
10
10
10
0
0
0
0
0
0
external
network
54
0
stub network
point to point
link
broadcast
network
external
network
Notes: If an external network annouces its aggregated routes, it is possible to take them into account.

## Slide 34: (b) Path Computation
Performed locally, based on topology database
Computes one or several best paths to every destination from this node
Best Path = shortest for OSPF
OSPF uses Dijkstra’s shortest path
  the best known algorithm for centralized operation
Paths are computed independently at every node
  synchronization of databases guarantees absence of persistent loops
  every node computes a shortest path tree rooted at self

## Slide 35: LS: Summary
All nodes compute their own topology database
  represents the whole network
  strongly synchronized
All nodes compute their best path tree to all destinations
Routing tables are built from the tree
  used for next hop routing only
LS versus DV
  LS avoids convergence problems of DV
  supports flexible cost definitions
  LS is much more complex

## Slide 36: 2. Divide large networks
Why divide large networks?
Cost of computing routing tables
  update when topology changes
  SPF algorithm
    n routers, k links
    complexity O(n*k)
  size of DB, update messages grows with the network size
Use hierarchical routing to limit the scope of updates and computational overhead
  divide the network into several areas
  independent route computing in each area
  inject aggregated information on routes into other areas
We explain hierarchical routing the OSPF way
  IS-IS does things a bit differently

## Slide 37: Hierarchical Routing
A large OSPF domain can be configured into areas
  one backbone area (area 0)
  non backbone areas (areas numbered other than 0)
All inter-area traffic goes through area 0
  strict hierarchy
Inside one area: link state routing as seen earlier
  one topology database per area
area 0
B1
X3
X1
X4
A1
area 2
area 1
X1
X3
X4
B2
A2

## Slide 38: Principles
Routing method used in the higher level:
  distance vector
  no problem with loops - one backbone area
Mapping of higher level nodes to lower level nodes
  area border routers (inter-area routers) belong to both areas
Inter-level routing information
  summary link state advertisements (LSA) from other areas are injected into the local topology databases

## Slide 39: Example
Assume networks n1 and n2 become visible at time 0. Show the topology databases at all routers
area 0
B1
X4
X1
X3
A1
area 2
area 1
X2
X6
X5
B2
A2
n1
n2
10
10
10
6
6
6
6
6
6
10
10
10

## Slide 40: Hints
  All routers in area 2 propagate the existence of n1 and n2, directly attached to B1 (resp. B2). Draw the topology database in area 2.
  Area border routers X4 and X6 belong to area 2, thus they can compute their distances to n1 and n2
  Area border routers X4 and X6 inject their distances to n1 and n2 into the area 0 topology database (item 3 of the principle). The corresponding summary link state record is propagated to all routers of area 0. Draw now the topology database in area 0.
  All routers in area 0 can now compute their distance to n1 and n2, using their distances to X4 and X6, and using the principle of distance vector (item 1 of the principle). Do the computation for X3 and X5.
  Area border routers X3 and X5 inject their distances to n1 and n2 into the area 1 topology database (item 3 of the principle). Draw now the topology database in area 1.

## Slide 41: Solution
area 0
B1
X4
X1
X3
A1
area 2
area 1
X2
X6
X5
B2
A2
n1
n2
10
10
10
6
6
6
6
6
6
10
10
10
n2
10
n1
n2
area 2 topology database
area 0 topology database
n1, d=10
n2, d=16
n1, d=16
n2, d=10
n1, d=28
n2, d=22
n1, d=22
n2, d=16
area 1 topology database

## Slide 42: Comments
Distance vector computation causes none of the RIP problems
  strict hierarchy: no loop between areas
External and summary LSA for all reachable networks are present in all topology databases of all areas
  most LSAs are external
  can be avoided in configuring some areas as terminal: use default entry to the backbone
Area partitions require specific support
  partition of non-backbone area is handled by having the area 0 topology database keep a map of all area connected components
  partition of backbone cannot be repaired; it must be avoided; can be handled by backup virtual area 0 links through non backbone area

## Slide 43: Example of issue : partitioned backbone
area 0
B1
X4
X1
X3
A1
area 2
area 1
X2
X6
X5
B2
A2
n1
n2
10
10
10
6

6
6

6
10
10
No connectivity between areas via backbone
There is a route through Area 2
Virtual link
  X4 and X6 configure a virtual link through Area 2
  virtual link entered into the database, metric = sum of links
10

## Slide 44: 3. The OSPF Protocol
OSPF (Open Shortest Path First)
  IETF standard for internal routing
  used in large networks (ISPs)
Link State protocol + Hierarchical

## Slide 45: Designated routers
Number of neighbours
  if n routers, n(n-1)/2 neighbors
Designated router on a LAN is used to save flooding
  n-1 neighbors
  elected automatically
  flooding
    advertise to 224.0.0.6 (all designated routers)
    flooded to 224.0.0.5 (all routers)
  back-up designated router
    listens to advertisements, but does not flood
    failure of the designated router detected by Hello
      back-up becomes designated router
l1
A
B
D
C
A
B
D
C
A
B
D
C
A
B
D
C
Notes:   back-up designated router has synchronized DB with designated router
  back-up designated router listens to announce, but does not flood

## Slide 46: OSPF Components
On top of IP (protocol type = 89)
Multicast
  224.0.0.5 - all routers of a link
  224.0.0.6 - all designated and backup routers
Sub-protocols
  Hello to identify neighbors, elect a designated and a backup router
  Database description to diffuse the topology between adjacent routers
  Link State to request, update, and ack the information on a link (LSA - Link State Advertisement)
LSA
  tagged with the router Id and checksum
  5 different types

## Slide 47: Classification of routers
Internal routers
  a router with all directly connected networks belonging to the same area
Area border routers
  attached to multiple areas
  condense LSA of their attached areas for distribution to the backbone
Backbone routers
  a router that has an interface to the backbone area
AS boundary routers
  exchange routing information with routers belonging to other AS

## Slide 48: Classification of routers
area 0
B1
X4
X1
X3
A1
area 2
area 1
X2
X6
X5
B2
A2
n1
n2
10
10
10
6
6
6
6
6
6
10
10
10
AS-boundary router
backbone router
area border router
internal router

## Slide 49: OSPF protocol PDUs
OSPF protocol type = 1
  Hello
OSPF protocol type = 2
  Database description
OSPF protocol type = 3
  Link State Request
OSPF protocol type = 4
  Link State Update
OSPF protocol type = 5
  Link State Ack

## Slide 50: TOS and metric
TOS
  mapping of 4 IP TOS bits to a decimal integer
  0 - normal service
  2 - minimize monetary cost
  4 - maximize reliability
  8 - maximize throughput
  16 - minimize delay
Metric
  time to send 100 Mb over the interface
  C = 108/bandwidth
  1 if greater than 100 Mb/s
  can be configured by administrator
Notes: TOS and metric in OSPF refer to Type of Service (from legacy IP headers) and cost metric, which together determine the best path by considering both bandwidth and service priorities.
TOS Mapping
qTOS ("quantized TOS") maps the 4 TOS bits from the IP header (Delay, Throughput, Reliability, Cost) to a decimal integer value (0–31). OSPF uses this to select paths matching the packet's QoS needs.​
0: Normal service (default, no special requirements).
2: Minimize monetary cost.
4: Maximize reliability.
8: Maximize throughput.
16: Minimize delay.
Routers prefer paths with matching or better TOS metrics; if none match, fall back to TOS 0.
OSPF Metric (Cost)
The metric (or cost) measures path preference, calculated as Reference Bandwidth / Interface Bandwidth.
Formula: (default reference bandwidth = 100 Mbps).
  Example: 10 Mbps link → Cost = 10.
  100 Mbps → Cost = 1.
  Faster than 100 Mbps (e.g., 1 Gbps) → Cost = 1 (minimum).
Administrator override: Manually set via ip ospf cost X on interfaces.
Total path cost = sum of interface costs; lowest cost wins.
How They Work Together
OSPF advertises TOS 0 cost by default in LSAs (Type 1, 2).
ABRs propagate TOS-specific costs (qTOS values) as additional metrics in Type 3 LSAs for inter-area routing.
Path selection: First by TOS match, then by lowest metric sum. Modern OSPF often ignores TOS (defaults to 0) unless explicitly configured.
This legacy feature (from RFC 1583) enables QoS-aware routing but is rarely used today, favoring traffic engineering elsewhere.
TOS and metric in OSPF refer to Type of Service (from legacy IP headers) and cost metric, which together determine the best path by considering both bandwidth and service priorities.
TOS Mapping
qTOS ("quantized TOS") maps the 4 TOS bits from the IP header (Delay, Throughput, Reliability, Cost) to a decimal integer value (0–31). OSPF uses this to select paths matching the packet's QoS needs.​
0: Normal service (default, no special requirements).
2: Minimize monetary cost.
4: Maximize reliability.
8: Maximize throughput.
16: Minimize delay.
Routers prefer paths with matching or better TOS metrics; if none match, fall back to TOS 0.
OSPF Metric (Cost)
The metric (or cost) measures path preference, calculated as Reference Bandwidth / Interface Bandwidth.
Formula: 𝐶=10^8/"bandwidth in bps" (default reference bandwidth = 100 Mbps).
  Example: 10 Mbps link → Cost = 10.
  100 Mbps → Cost = 1.
  Faster than 100 Mbps (e.g., 1 Gbps) → Cost = 1 (minimum).
Administrator override: Manually set via ip ospf cost X on interfaces.
Total path cost = sum of interface costs; lowest cost wins.
How They Work Together
OSPF advertises TOS 0 cost by default in LSAs (Type 1, 2).
ABRs propagate TOS-specific costs (qTOS values) as additional metrics in Type 3 LSAs for inter-area routing.
Path selection: First by TOS match, then by lowest metric sum. Modern OSPF often ignores TOS (defaults to 0) unless explicitly configured.
This legacy feature (from RFC 1583) enables QoS-aware routing but is rarely used today, favoring traffic engineering elsewhere.

## Slide 51: Convergence
Timer | Value | Purpose
LS Refresh | 30 min (1800 sec) | OSPF routers flood updated LSAs domain-wide to prevent aging out.
MaxAge (Route Timeout) | 1 hour (3600 sec) | LSAs invalid after this; removed from LSDB if not refreshed.
Dead Interval (Failure Detection) | 40 sec (4 × Hello) | Neighbor declared down if no Hello received; triggers SPF recalc.
SPF Throttle (Dijkstra Interval) | 30 sec (min) | Minimum time between SPF recomputations to avoid overload.
Reconfiguration Time | ~70 sec | Total convergence after config change (Hello dead + SPF delays).

## Slide 52: Convergence - Proposals
Proposal | Value | Benefit
Hello | Every 100 ms | Ultra-fast neighbor detection.
SPF | Immediately (on change) | Instant Dijkstra recompute, no throttling.
Proposals cut reconvergence from ~70 sec to sub-second using Bidirectional Forwarding Detection (BFD) for Hellos

## Slide 53: Conclusion
OSPF vs. RIP
  much more complex, but presents many advantages
    no count to infinity
    no limit on the number of hops (OSPF topologies limited by Network and Router LSA size (max 64KB) to O(5000) links)
    less signaling traffic (LS Update every 30 min)
    advanced metric
    large networks - hierarchical routing
  most of the traffic when change in topology
    but periodic Hello messages
    in RIP: periodic routing information traffic
  drawback
    difficult to configure

## Slide 54: a simple ospf lab
single-area

## Slide 55: lab topology
Area ID
10.0.3.0/24
10.0.1.0/24
10.0.2.0/24
bb0
eth0
3
eth1
3
D
B
C
0.0.0.0
10.0.0.0/24
A
bb1
eth0
1
eth1
1
45
10
eth0
2
eth1
1
bb2
10
10
eth1
2
eth0
2
bb3
7
10
bb4
eth1
2
eth0
1
10
10
36
21
ospf cost for exiting the interface

## Slide 56: lab description
single (backbone) area (0.0.0.0)
each interface is assigned an ospf cost
  default: 10
  we have tweaked the costs to force paths taken by traffic
to set interface costs:
  interface eth1 ospf cost 45

## Slide 57: (some) shortest paths
10.0.3.0/24
10.0.1.0/24
10.0.2.0/24
bb0
eth0
3
eth1
3
D
B
C
0.0.0.0
10.0.0.0/24
A
bb1
eth0
1
eth1
1
45
10
eth0
2
eth1
1
bb2
10
10
eth1
2
eth0
2
bb3
7
10
bb4
eth1
2
eth0
1
10
10
36
21
Area ID
ospf cost for exiting the interface
shortest path to reach:
10.0.2.0/24
shortest path to reach:
10.0.3.0/24

## Slide 58: experiments
perform traceroutes from/to different interfaces
perform a traceroute from bb1 to 10.0.2.1
  what path is the traceroute expected to take?
  what path are ICMP replies expected to take?
perform a traceroute from bb1 to 10.0.3.2
  what path is the traceroute expected to take?
  observe the interplay between ospf routes and directly connected networks (i.e., perform a show ip route in frr)
try to alter the costs and observe the effect of the changes

## Slide 59: experiments
access the ospfd cli (or the vtysh cli) on the various routers and issue the following commands:
  show ip ospf route
  show ip ospf interface
  show ip ospf neighbor
  show ip ospf database
check that the lsdb is exactly the same for all routers

## Slide 60: designated routers (router interfaces designated for each network)
for each network, one of the interfaces attached to that network is elected as designated (dr)
priority-based election, using hello packets
  the router (interface) sending hello packets with highest piority wins the election
  break ties on highest router id
    by default, a router id is the address of one of its interfaces
  priority[0,255]
    default priority: 1
    priority=0  never become a dr
a backup dr (i.e., the one with second highest priority) is also elected, to quickly recover from dr failures

## Slide 61: designated routers (router interfaces designated for each network)
a change of the dr is a change in ospf’s topology model (new lsas are sent)
for this reason, the dr is changed infrequently
  if a router with high priority wakes up and finds that a dr already exists, it accepts that dr

## Slide 62: designated routers (router interfaces designated for each network)
10.0.3.0/24
10.0.1.0/24
10.0.2.0/24
bb0
eth0
3
eth1
3
D
B
C
0.0.0.0
10.0.0.0/24
A
bb1
eth0
1
eth1
1
eth0
2
eth1
1
bb2
eth1
2
eth0
2
bb3
bb4
eth1
2
eth0
1
Area ID
designated
10.0.3.1
10.0.3.2
router id
10.0.2.2
10.0.1.1
10.0.2.3

## Slide 63: designated routers (router interfaces designated for each network)
bb1# show ip ospf interface
eth0 is up
ifindex 20, MTU 1500 bytes, BW 10000 Mbit <UP,BROADCAST,RUNNING,MULTICAST>
Internet Address 10.0.0.1/24, Broadcast 10.0.0.255, Area 0.0.0.0
MTU mismatch detection: enabled
Router ID 10.0.3.1, Network Type BROADCAST, Cost: 10
Transmit Delay is 1 sec, State DR, Priority 1
Designated Router (ID) 10.0.3.1 Interface Address 10.0.0.1/24
Backup Designated Router (ID) 10.0.2.3, Interface Address 10.0.0.3
Saved Network-LSA sequence number 0x80000002
Multicast group memberships: OSPFAllRouters OSPFDesignatedRouters
Timer intervals configured, Hello 10s, Dead 40s, Wait 40s, Retransmit 5
Hello due in 4.193s
Neighbor Count is 2, Adjacent neighbor count is 2
eth1 is up
ifindex 22, MTU 1500 bytes, BW 10000 Mbit <UP,BROADCAST,RUNNING,MULTICAST>
...
bb1
designated
router id
bb1
eth0
1
eth1
1
10.0.3.1

## Slide 64: ospf’s view of the network
by exchanging link state update packets, every router learns about the complete network topology, that is:
  routers
  subnets
  adjacencies between routers and networks

## Slide 65: ospf’s view of the network
bb0# show ip ospf database
bb0
for router lsas, the Link ID is the router’s id

## Slide 66: ospf’s view of the network
OSPF Router with ID (10.0.2.3)
Router Link States (Area 0.0.0.0)
Link ID ADV Router Age Seq# CkSum Link count
10.0.1.1 10.0.1.1 743 0x80000008 0xdfff 2
10.0.2.2 10.0.2.2 743 0x80000008 0xd9ff 2
10.0.2.3 10.0.2.3 742 0x8000000a 0xd9d4 2
10.0.3.1 10.0.3.1 747 0x80000009 0x268e 2
10.0.3.2 10.0.3.2 752 0x80000008 0x4091 2
bb0
0.0.0.0
bb1
bb2
bb3
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
for router lsas, the Link ID is the router’s id
bb0
bb4

## Slide 67: ospf’s view of the network
Net Link States (Area 0.0.0.0)
Link ID ADV Router Age Seq# CkSum
10.0.0.1 10.0.3.1 749 0x80000002 0x69a9
10.0.1.2 10.0.2.2 743 0x80000001 0x69bb
10.0.2.1 10.0.3.2 752 0x80000002 0x729a
10.0.3.2 10.0.3.2 753 0x80000001 0x6bb3
bb0
0.0.0.0
bb1
bb2
bb3
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
for network lsas, the Link ID is the dr’s address
10.0.3.2
10.0.1.2
D
B
10.0.0.1
A
10.0.2.1
bb0
C
bb4

## Slide 68: ospf’s view of the network
bb0# show ip ospf database router
Link State ID: 10.0.1.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.1
bb0
0.0.0.0
bb1
bb2
bb3
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
10.0.3.2
10.0.1.2
D
B
10.0.0.1
A
10.0.2.1
bb0
C
bb4

## Slide 69: ospf’s view of the network
bb0# show ip ospf database router
Link State ID: 10.0.1.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.1
bb0
0.0.0.0
bb1
bb2
bb3
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
10.0.3.2
10.0.1.2
D
B
we consider this router (bb2)
10.0.0.1
A
10.0.2.1
bb0
C
bb4

## Slide 70: ospf’s view of the network
bb0# show ip ospf database router
Link State ID: 10.0.1.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.1
bb0
0.0.0.0
bb1
bb3
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
10.0.3.2
10.0.1.2
D
this router interface...
...is connected to the subnet represented by this dr
bb2
B
eth0
2
eth1
1
10.0.0.1
A
10.0.2.1
bb0
C
bb4

## Slide 71: ospf’s view of the network
bb0# show ip ospf database router
Link State ID: 10.0.1.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.1
bb0
0.0.0.0
bb1
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
10.0.3.2
10.0.1.2
D
bb2
eth0
2
eth1
1
10.0.0.1
A
B
bb3
10.0.2.1
eth0
2
eth1
2
bb0
C
bb4

## Slide 72: ospf’s view of the network
bb0# show ip ospf database router
Link State ID: 10.0.1.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.1.2
(Link Data) Router Interface address: 10.0.1.1
bb0
0.0.0.0
bb1
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
10.0.3.2
D
bb2
eth0
2
eth1
1
10.0.0.1
A
B
bb3
10.0.2.1
eth0
2
eth1
2
bb0
C
bb4

## Slide 73: ospf’s view of the network
Link State ID: 10.0.2.3
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.3
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.2.1
(Link Data) Router Interface address: 10.0.2.3
bb0
bb0
0.0.0.0
bb1
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
10.0.3.2
D
bb2
eth0
2
eth1
1
10.0.0.1
B
bb3
10.0.2.1
eth0
2
eth1
2
A
C
eth0
3
3
eth1
bb4

## Slide 74: ospf’s view of the network
Link State ID: 10.0.3.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.1
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.3.2
(Link Data) Router Interface address: 10.0.3.1
bb0
bb0
0.0.0.0
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
10.0.3.2
bb2
eth0
2
eth1
1
10.0.0.1
B
bb3
10.0.2.1
eth0
2
eth1
2
C
eth0
3
3
eth1
A
bb1
D
eth0
1
eth1
1

## Slide 75: ospf’s view of the network
Link State ID: 10.0.3.1
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.0.1
(Link Data) Router Interface address: 10.0.0.1
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.3.2
(Link Data) Router Interface address: 10.0.3.1
bb0
bb0
0.0.0.0
bb4
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
10.0.3.2
bb2
eth0
2
eth1
1
B
bb3
10.0.2.1
eth0
2
eth1
2
C
eth0
3
3
eth1
A
bb1
D
eth0
1
eth1
1

## Slide 76: ospf’s view of the network
Link State ID: 10.0.3.2
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.2.1
(Link Data) Router Interface address: 10.0.2.1
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.3.2
(Link Data) Router Interface address: 10.0.3.2
bb0
bb0
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
10.0.3.2
bb2
eth0
2
eth1
1
B
bb3
10.0.2.1
eth0
2
eth1
2
eth0
3
3
eth1
A
bb1
eth0
1
eth1
1
eth0
1
C
bb4
eth1
2
D

## Slide 77: ospf’s view of the network
Link State ID: 10.0.3.2
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.2.1
(Link Data) Router Interface address: 10.0.2.1
Link connected to: a Transit Network
(Link ID) Designated Router address: 10.0.3.2
(Link Data) Router Interface address: 10.0.3.2
bb0
bb0
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database router has been summarized
bb2
eth0
2
eth1
1
B
bb3
eth0
2
eth1
2
eth0
3
3
eth1
A
bb1
eth0
1
eth1
1
eth0
1
C
bb4
eth1
2
D

## Slide 78: ospf’s view of the network
bb0# show ip ospf database network
bb0
bb0
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database network has been summarized
bb2
eth0
2
eth1
1
B
bb3
eth0
2
eth1
2
eth0
3
3
eth1
A
bb1
eth0
1
eth1
1
eth0
1
C
bb4
eth1
2
D

## Slide 79: ospf’s view of the network
Link State ID: 10.0.0.1 (address of Designated Router)
Advertising Router: 10.0.3.1
Network Mask: /24
Attached Router: 10.0.3.1
Attached Router: 10.0.1.1
Attached Router: 10.0.2.3
bb0
bb0
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database network has been summarized
bb2
eth0
2
B
bb3
eth0
2
eth1
2
bb1
eth0
1
eth0
1
C
bb4
eth1
2
D
eth0
3
3
eth1
eth1
1
eth1
1
10.0.0.0/24
A

## Slide 80: ospf’s view of the network
Link State ID: 10.0.1.2 (address of Designated Router)
Advertising Router: 10.0.2.2
Network Mask: /24
Attached Router: 10.0.1.1
Attached Router: 10.0.2.2
bb0
bb0
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database network has been summarized
bb2
eth0
2
B
bb3
eth0
2
eth1
2
A
bb1
eth0
1
eth0
1
C
bb4
eth1
2
D
eth0
3
3
eth1
eth1
1
eth1
1
10.0.1.0/24
10.0.0.0/24

## Slide 81: ospf’s view of the network
Link State ID: 10.0.2.1 (address of Designated Router)
Advertising Router: 10.0.3.2
Network Mask: /24
Attached Router: 10.0.3.2
Attached Router: 10.0.2.2
Attached Router: 10.0.2.3 █
bb0
bb0
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database network has been summarized
bb2
eth0
2
B
bb3
eth0
2
eth1
2
A
bb1
eth0
1
eth0
1
bb4
eth1
2
D
eth1
1
eth1
1
eth0
3
3
eth1
10.0.1.0/24
10.0.0.0/24
10.0.2.0/24
C

## Slide 82: ospf’s view of the network
Link State ID: 10.0.3.2 (address of Designated Router)
Advertising Router: 10.0.3.2
Network Mask: /24
Attached Router: 10.0.3.1
Attached Router: 10.0.3.2 █
bb0
bb0
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
note: the output of show ip ospf database network has been summarized
bb2
eth0
2
B
bb3
eth0
2
eth1
2
A
bb1
eth0
1
C
bb4
eth1
2
eth1
1
eth0
3
3
eth1
eth0
1
eth1
1
10.0.1.0/24
10.0.0.0/24
10.0.2.0/24
10.0.3.0/24
D

## Slide 83: ospf’s view of the network
root@bb0:~# vtysh -e "show ip ospf interface" | egrep "eth|Cost"
eth0 is up
Router ID 10.0.2.3, Network Type BROADCAST, Cost: 21
eth1 is up
Router ID 10.0.2.3, Network Type BROADCAST, Cost: 36
█
bb0
bb0
0.0.0.0
10.0.3.1
10.0.3.2
10.0.2.2
10.0.1.1
10.0.2.3
bb2
eth0
2
B
bb3
eth0
2
eth1
2
A
bb1
eth0
1
C
bb4
eth1
2
eth1
1
eth0
3
3
eth1
eth0
1
eth1
1
10.0.1.0/24
10.0.0.0/24
10.0.2.0/24
10.0.3.0/24
D
ospf interface costs can be queried on all routers
a shortcut to quickly get the cost
36
21

## Slide 84: neighborhood
router neighbors can be shown by using the show ip ospf neighbor command
note: lsas are only sent between neighbors in Full state (i.e., capable of a bidirectional exchange of information); reaching the Full state requires that:
  neighbors have been discovered (using hello packets)
  bidirectional communication is possible
  a designated router has been elected
once reached, routers immediately synchronize their lsdbs
bb0# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface RXmtL RqstL DBsmL
10.0.3.1 1 Full/DR 30.462s 10.0.0.1 eth0:10.0.0.3 0 0 0
10.0.1.1 1 Full/DROther 30.462s 10.0.0.2 eth0:10.0.0.3 0 0 0
10.0.3.2 1 Full/DR 31.587s 10.0.2.1 eth1:10.0.2.3 0 0 0
10.0.2.2 1 Full/DROther 31.586s 10.0.2.2 eth1:10.0.2.3 0 0 0
bb0-frr# █
bb0

## Slide 85: ospf routing table
To dump the ospf routing table use show ip ospf route
bb0# show ip ospf route
============ OSPF network routing table ============
N 10.0.0.0/24 [21] area: 0.0.0.0
directly attached to eth0
N 10.0.1.0/24 [31] area: 0.0.0.0
via 10.0.0.2, eth0
N 10.0.2.0/24 [36] area: 0.0.0.0
directly attached to eth1
N 10.0.3.0/24 [46] area: 0.0.0.0
via 10.0.2.1, eth1
============ OSPF router routing table =============
============ OSPF external routing table ===========
bb0

## Slide 86: ospf routing table
To dump the ospf routing table use show ip ospf route
bb0# show ip ospf route
============ OSPF network routing table ============
N 10.0.0.0/24 [21] area: 0.0.0.0
directly attached to eth0
N 10.0.1.0/24 [31] area: 0.0.0.0
via 10.0.0.2, eth0
N 10.0.2.0/24 [36] area: 0.0.0.0
directly attached to eth1
N 10.0.3.0/24 [46] area: 0.0.0.0
via 10.0.2.1, eth1
============ OSPF router routing table =============
============ OSPF external routing table ===========
bb0
route cost

## Slide 87: experiments
issue the show ip ospf database and show ip ospf neighbor commands on different routers
capture and look at exchanged ospf packets using tcpdump

## Slide 88: ospf is fast at detecting topology changes
case #1: link fault
  bring down a single network interface using ip link
    the change is immediately propagated by the router inside lsa packets
    routing tables are immediately updated (show ip ospf route)

## Slide 89: ospf is fast at detecting topology changes
case #1: link fault
  bring down a single network interface using ip link
    the change is immediately propagated by the router inside lsa packets
    routing tables are immediately updated (show ip ospf route)
    the lsdb is handled a little differently...

## Slide 90: ospf is fast at detecting topology changes
case #1: link fault
  bring down a single network interface using ip link
    if this brings down a dr, the information is immediately flushed from the lsdb(s)...
      ...and eventually reannounced when a dr is re-elected
    otherwise, ospf waits expiry of the RouterDeadInterval timer (default: 40s) before removing the adjacency from the lsdb (show ip ospf database network)
      note: networks that are connected to one router only, called stub networks, are only visible using show ip ospf database router

## Slide 91: ospf is fast at detecting topology changes
case #1: link fault
  bring down a single network interface using ip link
overall reaction time (estimated)
min
max
0
RouterDeadInterval

## Slide 92: ospf is (often) fast at detecting topology changes
case #2: router fault
  bring down a router (by crashing it or by shutting down all its interfaces simultaneously)
  the router has no chance to propagate lsas
    the change cannot be immediately propagated
    neighboring routers can only realize it (and update routing tables) after expiry of the RouterDeadInterval timer

## Slide 93: ospf is (often) fast at detecting topology changes
case #2: router fault
  bring down a router (by crashing it or by shutting down all its interfaces simultaneously)
  after the change has been propagated...
    ...lsdb information about networks for which the failed router was not dr is immediately flushed from other routers’ lsdbs
      the dr takes care of sending appropriate lsas
    ...lsdb information about networks for which the failed router was dr (including those where a dr will be re-elected) and about routers is more “tough”
      ospf waits for the lsa to expire (expiration happens when the age of the lsa reaches the MaxAge value of 1 hour) before taking any actions
last update: Nov 2018

## Slide 94: ospf is (often) fast at detecting topology changes
case #2: router fault
  bring down a router (by crashing it or by shutting down all its interfaces simultaneously)
overall reaction time (estimated)
min
max
RouterDeadInterval
MaxAge

## Slide 95: lab: ospf-multiarea

## Slide 96: ospf areas
an abstraction that simplifies administration and improves scalability
  the topology of an area is invisible from the outside
  routers internal to a given area don’t see the detailed external topology
each area runs a separate instance of the link state routing algorithm
  all routers in an area construct the same lsdb
  each router keeps a distinct lsdb for each area it belongs to

## Slide 97: ospf areas
identified by a 32-bit number, often in dotted decimal notation (1.2.3.4)
  different interfaces of the same router can be assigned to different areas
  each
    router interface...
    network...
    router adjacency...
  ...is associated with a single area

## Slide 98: area types
backbone (0.0.0.0)
  must be (virtually) connected
  all other areas are connected to it
  contains all the area border routers
stub
  does not receive advertisements of external routes
  internal nodes are offered a default route
  cannot contain autonomous system boundary routers
  the backbone can’t be a stub area
transit
  used to pass traffic from one adjacent area to another, via virtual links

## Slide 99
last update: Nov 2018
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
backbone
stub
stub
stub

## Slide 100: router types
internal router
  all interfaces belong to the same area
area border router (abr)
  connects one or more areas to the backbone
  keeps multiple lsdbs, one for each area
backbone router
  has at least one interface connected to the backbone
  an abr is always a backbone router
autonomous system boundary router (asbr)
  imports and floods routing information from other routing protocols (typically, bgp)
note: a router can be of more than one type

## Slide 101
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1

## Slide 102
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1
backbone
routers

## Slide 103
kathara – [ labs: ospf ]
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1
area border
routers

## Slide 104
kathara – [ labs: ospf ]
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1
internal
routers

## Slide 105
kathara – [ labs: ospf ]
10.0.3.0/24
10.0.1.0/24
bb4
10.0.2.0/24
10.0.0.0/24
bb0
eth0
3
eth1
3
D
A
B
C
0.0.0.0
eth0
2
eth2
1
E
100.0.0.0/30
1.1.1.1
2.2.2.2
3.3.3.3
r1
eth0
2
eth1
1
I
200.0.0.0/30
r2
J
200.0.1.0/24
r6
L
220.0.0.0/30
N
220.0.1.0/30
M
220.0.2.0/30
eth0
1
eth1
1
eth0
2
eth1
2
eth1
1
eth1
1
eth0
1
eth0
2
eth1
2
eth1
1
eth0
1
eth1
2
eth1
1
eth0
2
eth0
2
bb3
210.0.0.0/24
r5
eth2
2
eth2
1
H
130.0.0.0/30
bb2
eth3
1
r4
G
120.0.0.0/30
eth0
2
K
eth3
1
110.0.0.0/30
F
eth1
2
eth2
1
r3
bb1
90
100
default cost (10) is assumed where unspecified

## Slide 106: area configuration
area information is found in two places
  when enabling ospf on router interfaces network 200.0.0.0/16 area 1.1.1.1
  when specifying the area type (not required for the backbone) area 1.1.1.1 stub

## Slide 107: ospf path types
there are 4 path types
  intra-area
  inter-area
  external type 1
  external type 2
types can coexist in the same network
each type is preferred over the following ones

## Slide 108: ospf path types
intra-area paths
  calculated using the shortest-path tree

## Slide 109: ospf path types
inter-area paths
  abrs inject summary information inside each area, to make it aware of available destinations in other areas
    such information includes the cost of the shortest path from the abr to the destination
    if multiple subnets are summarized into a single network, the route cost will be the maximum cost to any of the component subnets
  an inter-area path is always composed of:
    an intra-area path from the source to the abr
    a backbone path between the source and destination areas
    an intra-area path to the destination

## Slide 110: ospf path types
external paths are learned from other routing protocols (e.g., bgp)
type 1: the cost is expressed in terms of
  the external (bgp) route cost* +
  the ospf cost to the asbr
  example with bgp cost=495, ospf cost=10: N E1 50.0.0.0/16 [505] tag: 0 via 10.0.1.2, eth1
* cost used when redistributing the protocol (bgp) into ospf; default for bgp=20; configurable by using redistribute bgp metric value

## Slide 111: ospf path types
external paths are learned from other routing protocols (e.g., bgp)
type 1: the cost is expressed in terms of
  the external (bgp) route cost* +
  the ospf cost to the asbr
type 2: the cost is expressed in terms of
  the external (bgp) route cost* only (distance to the asbr is only used to break ties)
  example with bgp cost=495, ospf cost=10: N E2 50.0.0.0/16 [10/495] tag: 0
  via 10.0.1.2, eth1

## Slide 112: ospf path types
external paths are learned from other routing protocols (e.g., bgp)
type 1: the cost is expressed in terms of
  the external (bgp) route cost* +
  the ospf cost to the asbr
type 2: the cost is expressed in terms of
  the external (bgp) route cost* only (distance to the asbr is only used to break ties)
metric type is user-configurable redistribute bgp metric-type 2 metric 495

## Slide 113: experiments
check that routers know detailed topology information only about their own area
r2# show ip ospf neighbor
Neighbor ID Pri State Up Time Dead Time Address Interface RXmtL RqstL DBsmL
200.0.0.1 1 Full/Backup 1m17s 32.279s 200.0.0.1 eth0:200.0.0.2 0 0 0
r2

## Slide 114: experiments
check that routers know detailed topology information only about their own area
r2# show ip ospf database router
OSPF Router with ID (200.0.1.1)
Router Link States (Area 1.1.1.1 [Stub])
...
Link State ID: 110.0.0.1
...
Number of Links: 1
Link connected to: a Transit Network
(Link ID) Designated Router address: 100.0.0.2
(Link Data) Router Interface address: 100.0.0.1
...
Link State ID: 200.0.0.1
...
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 100.0.0.2
(Link Data) Router Interface address: 100.0.0.2
...
Link connected to: a Transit Network
(Link ID) Designated Router address: 200.0.0.2
(Link Data) Router Interface address: 200.0.0.1
...
r2
note: the output has been summarized

## Slide 115: experiments
check that routers know detailed topology information only about their own area
r2# show ip ospf database network
OSPF Router with ID (200.0.1.1)
Net Link States (Area 1.1.1.1 [Stub])
LS age: 759
Options: 0x0 : *|-|-|-|-|-|-|-
LS Flags: 0x6
LS Type: network-LSA
Link State ID: 100.0.0.2 (address of Designated Router)
Advertising Router: 200.0.0.1
LS Seq Number: 80000001
Checksum: 0x09ec
Length: 32
Network Mask: /30
Attached Router: 110.0.0.1
Attached Router: 200.0.0.1
LS age: 763
Options: 0x0 : *|-|-|-|-|-|-|-
LS Flags: 0x3
LS Type: network-LSA
Link State ID: 200.0.0.2 (address of Designated Router)
Advertising Router: 200.0.1.1
LS Seq Number: 80000001
...
r2
note: the output has been summarized

## Slide 116: experiments
check what routers know about the outside of the area, using the show ip ospf database summary command
  in particular, check the Metric values, that show how far away the destination is from the advertising abr
check that routers in stub areas are offered a default route, whereas routers in the backbone are not
  also check what Metric is assigned to the default route

## Slide 117: experiments
r3# show ip ospf route
============ OSPF network routing table ============
N IA 0.0.0.0/0 [11] area: 2.2.2.2
via 110.0.0.1, eth1
via 120.0.0.1, eth0
...
r3
experiment ospf’s recovery capabilities
  when multiple equal cost routes are available, ospf keeps all of them
  check it by verifying what r3 knows about the default route
inter-area path
equal cost routes

## Slide 118: experiments
r3# show ip route
Codes: K - kernel route, C - connected, S - static, R - RIP, O - OSPF,
I - IS-IS, B - BGP, E - EIGRP, N - NHRP, T - Table, v - VNC,
V - VNC-Direct, A - Babel, F - PBR, f - OpenFabric, > - selected route,
* - FIB route, q - queued, r - rejected, b - backup t - trapped, o - offload failure
O>* 0.0.0.0/0 [110/11] via 110.0.0.1, eth1, weight 1, 00:18:15
* via 120.0.0.1, eth0, weight 1, 00:18:15
r3
experiment ospf’s recovery capabilities
  when multiple equal cost routes are available, ospf keeps all of them
  check it by verifying what r3 knows about the default route
  zebra performs the actual selection

## Slide 119: experiments
experiment ospf’s recovery capabilities
  when multiple equal cost routes are available, ospf keeps all of them
  check it by verifying what r3 knows about the default route
  zebra performs the actual selection
    now bring bb1’s eth3 down using ifconfig, wait a few seconds and check how the routing is changed
    bring bb1’s eth3 back up and check again how the routing is changed

## Slide 120: lab: ospf-complex

## Slide 121
last update: Nov 2018
kathara – [ labs: ospf ]
10.0.3.0/24
10.0.1.0/24
bb4
10.0.2.0/24
10.0.0.0/24
bb0
eth0
3
eth1
3
D
A
B
C
0.0.0.0
eth0
2
eth2
1
E
100.0.0.0/30
1.1.1.1
2.2.2.2
3.3.3.3
r1
eth0
2
eth1
1
I
200.0.0.0/30
r2
J
200.0.1.0/24
r6
L
220.0.0.0/30
N
220.0.1.0/30
M
220.0.2.0/30
eth0
1
eth1
1
eth0
2
eth1
2
eth1
1
eth1
1
eth0
1
eth0
2
eth1
2
eth1
1
eth0
1
eth1
2
eth1
1
eth0
2
eth0
2
bb3
as100r1
210.0.0.0/24
eth2
1
eth0
2
O
140.0.0.0/30
r5
50.0.0.0/16
AS10
AS100
eth2
2
eth2
1
H
130.0.0.0/30
bb2
eth3
1
r4
G
120.0.0.0/30
eth0
2
K
eth3
1
110.0.0.0/30
F
eth1
2
eth2
1
r3
bb1
90
100
default cost (10) is assumed where unspecified

## Slide 122: lab description
same as multiarea + some information is injected via bgp from an external as
  also, abrs are configured to just inject the default route area 1.1.1.1 stub no-summary
perform the same experiments as for the multiarea lab
  in addition, check asbr information using
    show ip ospf database asbr-summary
  also check that such information is not propagated inside stub areas

## Slide 123: a quick note about stub networks
“stub” = not used for transit
three possible situations:
kathara – [ labs: ospf ]
r2
J
200.0.1.0/24
eth1
1
ospf is enabled also on the stub network’s interface
the stub network is advertised in the entire ospf domain
interface uselessly sends hello packets
ospf is not enabled on the stub network’s interface
the stub network is advertised
the stub network is advertised as an AS-external route (hence, only through the backbone)
ospf is enabled on the stub network’s interface, which is configured as passive-interface
the stub network is advertised in the entire ospf domain
N/A
then
but
then
but
then
but

## Slide 124: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.