## Slide 1: FRRouting

## Slide 2: Summary
What is routing?
Kathara Implementation (lab on FRR)

## Slide 3: The network layer is the Inter-Net layer
At the beginning: networking technologies were
  Tied to a specific transmission medium (cable, ether)
  Very diverse (many different technologies and protocols, competing for a market)
  Aiming at connecting few local end-user devices ->local nets (or «subnets»)
  How did the architecture of the network looked like, at that time?

## Slide 4: Some drawing…

## Slide 5: The problem:
How to interconnect devices from different local nets, without creating a single big, local net (of the same technology)??

## Slide 6: Solution (well, one of the possible solutions)
Put all these local net technologies into a layer (the link layer)
Create a new layer on top of it, whose task is to deliver a message between any couple of end-user devices from any subnet to any subnet in the world
This layer has its own Interface names (IP addresses) and intermediate systems (called routers), just like any other subnet technology
Internet was born!

## Slide 7: How does the network layer work?
To answer, we look at the main functions it implements:
  Forwarding
  Routing
Let’s start from the Forwarding function.
And let us consider a single router:

## Slide 8: What is Forwarding?
Local process that takes place at a router and determines the output link for each packet
  Done individually, for each packet
Main ingredients:
Information on the packet’s network layer header (an identifier)
Forwarding tables at each router
Notes: How: read value from packet’s network-layer header, search forwarding table for output link

## Slide 9
Routing: How to populate forwarding tables (automatically)?
Through a routing process that, given the network topology:
It computes the path from every possible source to every possible destination
It configures accordingly the forwarding table at each router
Notes: Networks are too big and messy to do it by hand (errors)

## Slide 10
routing algorithm
network controller
Notes: Let’s talk a little bit about routing.
As stated in the previous slide, the goal of routing is to populate the forwarding tables of routers.
One option is to connect all the routers in the network to a logically centralized device, which we will call the “network controller,” and run, on that device, a centralized routing algorithm.
A network controller has a global view of the network, i.e., it knows where all the routers are and how they are interconnected, hence it can determine what each forwarding table should contain and communicate this information to each router.

## Slide 11
routing algorithm
routing algorithm
Notes: Another option is to run routing algorithms on the routers themselves. I.e., the routers exchange information with each other and collaborate to compute on their own what their forwarding tables should contain.
This is what mostly happens on the Internet today.

## Slide 12: Routing
Network-wide process that populates forwarding tables
How: routing algorithm run on a logically centralised network controller or the routers themselves

## Slide 13: Forwarding vs. routing
Routing populates forwarding tables to make forwarding possible
Forwarding uses forwarding tables to determine the output link for each packet
Notes: To conclude this first part, a network layer provides at least two basic functions: forwarding and routing. Forwarding relies on forwarding tables, while routing populate the forwarding tables that are needed for forwarding.

## Slide 14: Routing: Populate forwarding tables based on knowledge of paths
But… just any path between two subnets? Or the best?
Best in which sense? Which metric?

## Slide 15: We look at minimum cost routing
Goal: Find the cheapest route from each source router to each destination router
Notes: Quindi, l'obiettivo dell'instradamento del percorso meno costoso è trovare il percorso meno costoso (o percorso meno costoso) da ciascun router di origine a ciascun router di destinazione.

## Slide 16: Interior Routing
There are two types of routing methods
Within an Administrative Domain = Interior Routing Between Domains = Exterior Routing Problem solved by a routing protocol What does a routing protocol do? Find reachable destinations Find the best routes to destinations better in the sense of a metric

## Slide 17: Metrics
  Static metric: Not dependent on network status; For example:
    Number of nodes crossed ("hops") Link capability and static delay Cost
  Dynamic metric: depends on the state of the network
    Link load Current Packet Delay

## Slide 18: Simple routing methods How routing protocols work
Static configuration
only for very simple networks
Flooding
  each duplicate packet on each outbound link; loops prevented by packet ID or other mechanisms; Duplicate packets can be received at their destination Simple and robust
  No need for routing tables Rugged: Tolerates link or router failures optimal in a way The first package found the shortest route to the destination
  Expensive
  Lots of duplicate packets – little useful traffic
  used as an ingredient by ad-hoc routing methods for mobile devices (AODV, OLSR)
Source routing
  source writes the path to the packet header The router reads the next hop from the packet header, moves the pointer Path discovered via flooding

## Slide 19: Source Routing
A
B
2.2.4
IS
B
IS
IS
IS
A
SA DA RI data
1
2
3
1
2
1
3
1
3
4
3
2
2
4
A
B
2.2.4
A
B
2.2.4
Q. What are the paths that can be used from A to B ?
Example: A path is described by a sequence of port numbers

## Slide 20: Finding routes in Token Ring
B1
A
R1
R2
B4
R4
B3
B5
R5
B6
R6
B2
R3
B
An "All Route Broadcast" packet is generated by A. This creates 5 different packets.
1. A-R1-B1-R2-B2-R3
2. A-R1-B1-R2-B3-R5-B6-R6
3. A-R1-B1-R2-B3-R5-B5-R4
4. A-R1-B4-R4-B5-R5-B3-R2-R3
5. A-R1-B4-R4-B5-R5-B6-R6
2 of them reach B (numbers 2 and 5). B will choose the best one and communicate it to A, who will use it in future communications with B. route_1 = R1.B1.R2.B3.R5.B6.R6
route_2 = R1.B4.R4.B5.R5.B6.R6

## Slide 21: Other methods
Distance vector (Bellman-Ford)
  Routers only know their local state Link metrics and neighbor estimates Internal routing protocols (RIP, IGRP)
Link state
  Built on global state knowledge Topology database Global Optimization (Shortest Path First - Dijkstra) Interior Routing Protocols (OSPF)
Path vector
  No knowledge of the global status path: sequence of administrative domains with attributes Global optimization and policy routing
  Exterior routing protocols (BGP)

## Slide 22
Kathara Implementation (lab on FRR)

## Slide 23: preconditions
for this lab we assume you have chosen “kathara/frr” as the default image of your Kathará installation
  execute “kathara settings”
    select “choose default image”
    select “kathara/frr”
    exit from the settings procedure

## Slide 24: Hosts need routing
each host with a network stack performs some elementary routing
at the very least, the network stack may be used to access local services (e.g., Xorg)
the host must decide when a packet needs to be sent to the network interface card (nic) and when it needs to be bounced to the loopback interface (lo)
© Computer Networks Research Group Roma Tre
eth0
lo
nic
ip layer
?

## Slide 25: Questions
Is it ok to have hosts participate in routing algorithm together with routers?

## Slide 26: routing table
the ip layer uses a routing table to decide which is the interface the packet needs to be forwarded to
routing table
network netmask nexthop dev
200.3.24.0 255.255.255.0 12.0.0.4 eth1
193.2.0.0 255.255.248.0 11.0.0.2 eth0
100.4.5.0 255.240.0.0 11.0.0.3 eth0
0.0.0.0 0.0.0.0 11.0.0.2 eth0
eth0
lo
nic
ip layer
?
eth1
nic

## Slide 27: routers
eth0
lo
nic
ip layer
a router (also called gateway or intermediate-system)
  has more than one network interface card
  feeds incoming ip packets (that are not for the router itself) back in the routing process
    this operation is called relaying or forwarding
yes
no
eth1
nic
is it for me?

## Slide 28: routing protocols
routing protocols are used to automatically update routing tables, relieving administrators from the need to do it manually
routers (i.e., devices that run routing protocols) in Kathará are virtual machines that run a specific piece of software that implements routing protocols
FRRouting

## Slide 29: The FRRouting Suite
a free and open-source Internet routing protocol suite for Linux and Unix platforms

## Slide 30: about the FRRouting Suite
FRR is a software that implements some routing protocols
  rip (v1 and v2), ospf (v2 and v3), is-is
  bgp
  pim, ldp, bfd, babel, pbr, openfabric, vrrp, …
frr has its roots in the quagga project
  quagga is no longer supported
in turn, quagga was a community project that originated from (and superseded) the zebra project

## Slide 31: frr is a routing daemon
conf & logs
zebra
bgpd
ripd
ospfd
kernel
file access
connections
routing updates
bgpd>█
ripd>█
ospfd>█
zebra>█
conf & logs
Notes: FRRouting (FRR) operates as a suite of modular daemons that handle routing protocols and forwarding on Linux systems.
FRR uses zebra as the central routing information base (RIB) manager and forwarding daemon.
Protocol-specific daemons like bgpd (BGP), ospfd (OSPF), or ripd exchange routes with peers and update zebra via a proprietary protocol.
Daemons run as independent processes controlled by /etc/frr/daemons, where you enable them (e.g., bgpd=yes).
They load configs from files like frr.conf or per-daemon files.
Workflow
Protocol daemons learn routes via their protocols.
They push validated routes to zebra's RIB.
Zebra installs best routes into the kernel FIB via netlink and handles redistribution between protocols

## Slide 32: sample daemons configuration file
root@r1:~$ cat /etc/frr/daemons
# This file tells the frr package which daemons to start.
#
# Sample configurations for these daemons can be found in
# /usr/share/doc/frr/examples/.
#
# ...
#
bgpd=no
ospfd=no
ospf6d=no
ripd=yes
ripngd=no
...
the rip daemon will be started

## Slide 33: sample vtysh.conf configuration file
root@r1:~$ cat /etc/frr/vtysh.conf
no service integrated-vtysh-config
root@r1:~$
root@r1:~$
root@r1:~$
root@r1:~$
root@r1:~$
root@r1:~$ cat /etc/frr/vtysh.conf
service integrated-vtysh-config
with this command each daemon will
need its own configuration file (default)
a single configuration frr.conf file for
all daemons (recommended)

## Slide 34: a simple topology
r3
r2
r1
eth0
1
A
100.0.0.0/24
B
200.0.0.0/30
dev
ip
legend
last byte of ip address
network interface
subnet
assigned prefix
L
150.0.0.0/30
D
220.0.0.0/24
eth1
1
eth0
2
C
eth1
1
eth0
2
eth1
1
150.0.0.0/30

## Slide 35: launching the lab script
the lab configuration is such that
  three virtual hosts are created and connected to the right collision domains (virtual hubs)
  for each virtual host
    network interfaces are automatically configured
    frr configuration files are updated
  the frr routing daemon is automatically started
user@localhost:~$ cd kathara-lab_frr
user@localhost:~/kathara-lab_frr$ kathara lstart

## Slide 36: automatically start frr
to ease the startup of the lab is better to automatically start the frr
  the main daemon and all the routing protocols daemons are automatically started with frr
systemctl start frr
r1.startup

## Slide 37: a one-fits-all shell
instead of having to connect to each single daemon, users can interact with frr by using a built-in shell, called vtysh
the user is not prompted for a password
all the commands to manage all the routing daemons (including zebra itself) are available in this shell
root@r1:~$ vtysh
Hello, this is FRRouting (version 9.0.1).
Copyright 1996-2005 Kunihiro Ishiguro, et al.
r1#

## Slide 38: available vtysh commands
press ‘?’ at the command prompt to retreive all commands available
  here are displayed only the main ones
r1# ?
configure Configuration from vty interface
enable Turn on privileged mode command
exit Exit current mode and down to previous mode
no Negate a command or set its defaults
ping Send echo messages
quit Exit current mode and down to previous mode
show Show running system information
terminal Set terminal line parameters
write Write running configuration to memory, network, or terminal

## Slide 39: privileges on a router
sees noncritical information
sees critical information
performs elementary configurations that do not affect router behavior (e.g., set time and date)
commits changes
performs persistent configurations affecting the router behavior
configurator
privileged user
unprivileged user
configure
enable
disable
quit
default user

## Slide 40: inspecting the frr routing table
FIB entries from this table (marked with a ‘>’) are injected into the kernel routing table
© Computer Networks Research Group Roma Tre
r1# show ip route
Codes: K - kernel route, C - connected, S - static, R - RIP, O - OSPF,
I - IS-IS, B - BGP, E - EIGRP, N - NHRP, T - Table, v - VNC,
V - VNC-Direct, A - Babel, F - PBR, f - OpenFabric,
> - selected route, * - FIB route, q - queued, r - rejected, b - backup
t - trapped, o - offload failure
R>* 100.0.0.0/24 [120/3] via 200.0.0.1, eth0, weight 1, 00:01:32
R>* 150.0.0.0/30 [120/2] via 200.0.0.1, eth0, weight 1, 00:01:32
C>* 200.0.0.0/30 is directly connected, eth0, 00:01:33
C>* 220.0.0.0/24 is directly connected, eth1, 00:01:33

## Slide 41: inspecting the current configuration
r1# show running-config
Building configuration...
Current configuration:
!
frr version 9.0.1
frr defaults traditional
hostname r3
no ipv6 forwarding
no service integrated-vtysh-config
!
end
r1#
Notes: “prefix‑list defaults” and “access‑list defaults” refer to FRR’s behavior when no explicit permit/deny rule matches; “traditional” means using FRR’s classic Cisco‑like semantics where lists default to deny unless a rule permits traffic.

## Slide 42: some observations
the frr configuration language is “operational” and not “declarative”
  the configuration file is simply a list of configuration commands that would bring the router to its operative state
  it is not an abstract description of how the router should behave according to the configurator
you cannot remove a configuration command
  if the command has a certain string (e.g., “ipv6 forwarding”) in order to remove it you should issue the same string preceded by “no” (e.g., “no ipv6 forwarding”)

## Slide 43: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.