## Slide 1: RIP with FRRouting

## Slide 2: Recalls
What is RIP?
RIP with FRR

## Slide 3: The Distance-Vector routing algorithm
Based on routers’ interaction and cooperation during the computing phase
It works in rounds
At each round, each router takes as input:
  the router’s current set of least-cost paths
  That of all its neighbors
Output of each router:
  A new set of least-cost paths to every other router
Termination: When at every router, output==input
Notes: Distance-vector routing algorithm:
In each round, the instance of the algorithm running at each router takes as input the router’s current table plus the tables of its neighbors.
At the end, the instance of the algorithm running at each router produces as output the least-cost path to every other router in the network.

## Slide 4
x
x
y
0
-
y
v
v
1
2
-
-
-
-
-
from
to
y
2
1
3
z
v
1
x
z
-
-
-
x
x
y
-
1
y
v
-
-
0
-
z
-
-
-
z
-
3
-
x
y
v
-
-
y
v
z
-
-
-
-
-
3
1
z
-
-
0
x
x
-
y
v
v
-
-
2
-
0
z
-
-
-
z
-
1
-
Notes: Here is a second, a bit more complicated example:
In the beginning, each router knows how to reach only its direct neighbors.

## Slide 5
x
x
y
0
1
y
v
v
1
2
0
-
2
-
0
from
to
y
2
1
3
z
v
1
x
z
-
3
1
x
y
v
y
v
z
z
-
3
1
0
x
x
y
1
y
v
0
-
z
z
3
x
x
y
v
v
2
-
0
z
z
1
1
0
-
2
-
0
3
1
0
1
2
-
-
3
1
0
-
3
1
0
0
1
2
-
Notes: In the first round, all the neighbors exchange tables.
As a result, router x discovers a new path to router z, through router v, with cost 2+1=3…

## Slide 6
x
x
y
0
1
y
v
v
1
2
0
-
2
-
0
from
to
y
2
1
3
z
v
1
x
z
3
3
1
x
y
v
y
v
z
z
-
3
1
0
x
x
y
1
y
v
0
-
z
z
3
x
x
y
v
v
2
-
0
z
z
1
1
0
-
2
-
0
3
1
0
0
1
2
-
-
3
1
-
3
1
0
0
1
2
-
Notes: and updates its table accordingly (note that the new number 3 that appears in x’s table is purple, because it was computed based on information propagated through router v).
(Parenthesis: Router x actually discovers two new paths to router z: one through v, of cost 3, and one through y, of cost 4. It compares the two and determines that the one through v is better.)
Similarly, router z discovers a new path to router x, through router v, with cost 3…

## Slide 7
x
x
y
0
1
y
v
v
1
2
0
-
2
-
0
from
to
y
2
1
3
z
v
1
x
z
3
3
1
x
y
v
1
y
v
z
0
-
2
-
0
z
3
1
3
3
1
0
x
x
y
1
y
v
0
-
z
z
3
x
x
y
v
v
2
-
0
z
z
1
0
0
1
2
-
-
3
1
-
3
1
0
0
1
2
-
Notes: and updates its table accordingly.
At the same time, router y learns a new path to router v, through router x, with cost 1+2=3…

## Slide 8
x
x
y
0
1
y
v
v
1
2
0
-
2
-
0
from
to
y
2
1
3
z
v
1
x
z
3
3
1
x
y
v
1
y
v
z
0
-
2
-
0
z
3
1
3
3
1
0
x
x
y
1
y
v
0
3
z
z
3
x
x
y
v
v
2
-
0
z
z
1
0
0
1
2
-
-
3
1
-
3
1
0
0
1
2
-
Notes: and updates its table accordingly (note that the new number 3 that appears in y’s table is black, because it was computed based on information propagated by router x).
Similarly, router v learns a new path to router y, through router x, with cost 2+1=3…

## Slide 9
x
x
y
0
1
y
v
v
1
2
0
-
2
-
0
from
to
y
2
1
3
z
v
1
x
z
3
3
1
x
y
v
1
y
v
z
0
-
2
-
0
z
3
1
3
3
1
0
x
x
y
1
y
v
0
3
z
z
3
x
x
y
v
v
2
3
0
z
z
1
0
0
1
2
-
-
3
1
-
3
1
0
0
1
2
-
Notes: and updates its table accordingly.

## Slide 10
x
x
y
0
1
y
v
v
1
2
0
3
2
3
0
from
to
y
2
1
3
z
v
1
x
z
3
3
1
x
y
v
1
y
v
z
0
3
2
3
0
z
3
1
3
3
1
0
x
x
y
1
y
v
0
3
z
z
3
x
x
y
v
v
2
3
0
z
z
1
0
0
1
2
3
3
3
1
3
3
1
0
0
1
2
3
Notes: In the second round, all the neighbors exchange tables again.
This time, no router can improve any path with the new information that it has just received, so the algorithm is done.

## Slide 11: Distance-vector routing algorithm
Distributed algorithm
All routers run it “together”: neighbors exchange and react to each other’s messages
Notes: A distance-vector routing algorithm is a distributed algorithm, in the sense that all routers run it together: they exchange messages and they keep reacting to each other’s messages.

## Slide 12: Bellman-Ford algorithm
All neighbors exchange information
Each router checks whether it can improve current paths by leveraging the new information
Ends when no improvement is possible
Notes: The particular distance-vector routing algorithm that we discussed is called
the Bellman-Ford algorithm.
In summary:
At each step, all neighbors exchange tables.
Each router checks whether it can use the new information it just received to improve its current paths.
The algorithm ends when no improvement is possible.

## Slide 13
How to avoid routing loops?
We will see now how a naive implementation of the Bellman-Ford routing protocol can lead to routing loops
Notes: One of the main challenges in designing routing protocols

## Slide 14
x
z
y
7
2
1
2
0
1
x
y
y
z
z
3
1
0
x
y
y
z
z
3
1
0
2
0
1
Notes: Consider this 3-router network, where router y’s path to router x is direct, and router z’s path to router x is indirect, through router y.
Now suppose that link (x,y) breaks down.

## Slide 15
0
1
x
z
y
7
1
x
y
y
z
z
3
1
0
x
y
y
z
z
3
1
0
2
0
1
4
routing loop!
Notes: Router y immediately detects the problem, because it is directly connected to router x;
so, it realizes that it does not have a link to router x any more.
But, router y makes a mistake:
- It says: oh, router z can route to router x with cost 3.
- So, let me route to router x through router z, since I cannot route directly any more.
- Since I can route to router z with cost 1, the cost of this new indirect path to router x is 1 + 3 = 4.
So, at this point, we have a nice routing loop:
router z is routing to router x through router y
and router y is routing to router x through router z.
so, packets going to router x will ping-pong between routers y and z.

## Slide 16
0
1
x
z
y
7
1
x
y
y
z
z
3
1
0
x
y
y
z
z
3
1
0
4
0
1
4
routing loop!
Notes: Here is what happens next:
Routers y and z exchange tables.
Router z says:
- my path to router x is through router y;
- router y’s cost to router x has increased to 4;

## Slide 17
0
1
x
z
y
7
1
x
y
y
z
z
3
1
0
x
y
y
z
z
5
1
0
4
0
1
4
routing loop!
Notes: so let me update my cost to router x to 1+4=5.
And the loop persists.
Then the neighbors exchange tables again.

## Slide 18
0
1
x
z
y
7
1
x
y
y
z
z
5
1
0
x
y
y
z
z
5
1
0
4
0
1
4
routing loop!
Notes: Router y says:
- my path to router x is through router z;
- router z’s cost to router x has increased to 5;

## Slide 19
0
1
x
z
y
7
1
x
y
y
z
z
5
1
0
x
y
y
z
z
5
1
0
4
0
1
6
routing loop!
Notes: so, let me also update my cost to router x to 1+5=6.
And the loop persists.
Then the neighbors exchange tables again.

## Slide 20
0
1
x
z
y
7
1
x
y
y
z
z
5
1
0
x
y
y
z
z
5
1
0
6
0
1
6
routing loop!
Notes: The same story continues:
Router z says:
- my path to router x is through router y;
- router y’s cost to router x has increased to 6;

## Slide 21
0
1
x
z
y
7
1
x
y
y
z
z
5
1
0
x
y
y
z
z
7
1
0
6
0
1
6
routing loop!
Notes: so let me update my cost to router x to 7.
And the loop persists.
Then the neighbors exchange tables again.

## Slide 22
0
1
x
z
y
7
1
x
y
y
z
z
7
1
0
x
y
y
z
z
7
1
0
6
0
1
6
routing loop!
Notes: Router y says:
- my path to router x is through router z;
- router z’s cost to router x has increased to 7;

## Slide 23
0
1
x
z
y
7
1
x
y
y
z
z
7
1
0
x
y
y
z
z
7
1
0
6
0
1
8
routing loop!
Notes: so, let me update my cost to router x to 8.
And the loop persists.
Then the neighbors exchange tables again.

## Slide 24
0
1
x
z
y
7
1
x
y
y
z
z
7
1
0
x
y
y
z
z
7
1
0
8
0
1
8
routing loop!
Notes: Router z says:
- my path to router x is through router y;
- router y’s cost to router x has increased to 8;
- so, if I continue to route through router y, my cost to router x will become 9;
- I have a better path to router x: I have a direct path, of cost 7.

## Slide 25
0
1
x
z
y
7
1
x
y
y
z
z
7
1
0
x
y
y
z
z
7
1
0
8
0
1
8
routing loop!
count-to-infinity scenario
Notes: At this point, router z changes its path to router x: it routes to x through the direct link of cost 7 (note that the number 7 in z’s table has now become green, it indicate that it corresponds to a direct link).
This is where the routing loop ends.
The scenario I just described is called “count-to-infinity” (because the routers keep “counting,” i.e., increasing their costs to router x by 1).

## Slide 26: Problem with Bellman-Ford
Routing loop
  z routes through y, y routes through x
  y loses connectivity to x
  y decides to route through z
Can take very long to resolve
  count-to-infinity scenario
How to avoid them?
Notes: So: If we are not careful with the Bellman-Ford implementation (or any routing protocol implementation, for that matter), we may end up with routing loops, which may take a long time to resolve.

## Slide 27
x
z
y
7
2
1
2
0
1
x
y
y
z
z
∞
1
0
x
y
y
z
z
3
1
0
2
0
1
poisoned reverse
Notes: Here is a solution:
- If the path from router z to router x goes through router y,
- then router z tells router y that its cost to router x is infinity.
- In other words, router y should never try to route to router x through router z,
- because z is routing to x through y.
This technique is called *poisoned reverse*. This is because the “reverse path” (the path from y to z to x, in our example) is “poisoned” (i.e., y is not allowed to use it).
Now, if the link between x and y goes down, router y realizes that:
it cannot route to x directly
and it cannot route to x through z (because of the poisoned reverse).

## Slide 28
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
3
1
0
2
0
1
∞
poisoned reverse
∞
Notes: Hence, router y sets the cost of the path from itself to router x to infinity. Note that this infinity is NOT a poisoned reverse. It just indicates that the link from y to x is down, and y cannot route to x.

## Slide 29
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
3
1
0
0
1
∞
poisoned reverse
∞
∞
Notes: Then the neighbors exchange tables,
router z learns that router y has been disconnected from router x…

## Slide 30
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
7
1
0
0
1
∞
poisoned reverse
∞
∞
Notes: hence chooses the direct path to router x, which has cost 7, and updates its table accordingly.

## Slide 31
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
7
1
0
0
1
poisoned reverse
∞
∞
7
Notes: Then the neighbors exchange tables again,
Router y learns that router z has a path to router x of cost 7…

## Slide 32
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
7
1
0
0
1
poisoned reverse
∞
7
8
Notes: hence realizes that it (router y) can route to router x through router z with cost 1+7=8 and updates its table accordingly.
At this point, both routers have computed their paths to router x correctly.
Important: notice the poisoned reverse in router z’s table, which ensures that router z will never try to route to router x through router y.

## Slide 33: Solution
Poisoned reverse
  if z routes to x through y, z advertises to y that its cost to x is infinite
  y never decides to route to x through z
Algorithm re-converges quickly
  avoids count-to-infinity scenario
Notes: So: One way to avoid the count-to-infinity scenario is poisoned reverse, which enables the Bellman-Ford algorithm to re-converge quickly after a link failure.

## Slide 34
RIP with FRR

## Slide 35: The RIP protocol in Kathara’
RIP is a distance-vector routing protocol
  approach: send all your information to a few
  update your routing information based on what you hear
in this lab we will see an example of RIPv2 protocol on the FRRouting Suite

## Slide 36: sample frr.conf configuration file
root@pc1:~$ cat /etc/frr/frr.conf
!
! FRRouting configuration file
!
!
! RIP CONFIGURATION
!
router rip
network 100.1.0.0/16
!
log file /var/log/frr/frr.log
talk rip on some interface
send rip multicast packets to interfaces falling into this prefix

## Slide 37: Small network connected to Internet
r5
r4
r1
r3
r2

## Slide 38: The involved ip subnets
each circle represents a subnet
r5
r4
r1
r3
r2
L
B
A
H
E
C
D
G
F
I
legend

## Slide 39: Assigning ip addresses to subnets
100.1.4.0/24
r5
L
r4
r1
r3
B
100.1.2.0/24
A
100.1.1.0/24
H
100.1.0.12/30
E
100.1.0.0/30
100.2.0.0/30
r2
C
100.1.3.0/24
D
G
F
I
100.1.0.4/30
100.1.0.16/30
100.1.0.8/30
legend
ip subnet
assigned prefix
L
100.2.0.0/30

## Slide 40: Assigning ip addresses to subnets
r5
eth0
1
eth0
2
L
eth2
18
r4
eth3
14
eth1
9
eth2
1
eth0
6
eth1
10
r1
r3
eth3
1
eth2
1
B
100.1.2.0/24
A
100.1.1.0/24
H
100.1.0.12/30
E
100.1.0.0/30
100.2.0.0/30
r2
eth2
17
C
100.1.3.0/24
eth0
13
D
100.1.4.0/24
eth1
1
G
F
I
eth3
1
eth0
2
eth1
5
100.1.0.4/30
100.1.0.16/30
100.1.0.8/30
dev
ip
legend
last byte of ip address
network interface

## Slide 41: launching the lab
the lab configuration is such that the frr routing daemon is not automatically started
root@localhost:~$ cd kathara-lab_rip
root@localhost:~/kathara-lab_rip$ kathara lstart

## Slide 42: checking connectivity
towards a directly connected destination
root@r4:~$ ping 100.1.0.13
PING 100.1.0.13 (100.1.0.13) 56(84) bytes of data.
64 bytes from 100.1.0.13: icmp_seq=1 ttl=64 time=1.23 ms
64 bytes from 100.1.0.13: icmp_seq=2 ttl=64 time=0.592 ms
64 bytes from 100.1.0.13: icmp_seq=3 ttl=64 time=0.393 ms
--- 100.1.0.13 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2032ms
rtt min/avg/max/mdev = 0.393/0.741/1.238/0.360 ms

## Slide 43: checking connectivity
towards a remote destination
what’s going on?
root@r4:~$ ping 100.1.2.1
connect: Network is unreachable

## Slide 44: examining the kernel routing table
since no routing daemon is currently running, only directly connected destinations are known to the router
root@r4:~$ ip route
100.1.0.12/30 dev eth3 proto kernel scope link src 100.1.0.14
100.1.0.16/30 dev eth2 proto kernel scope link src 100.1.0.18
100.1.4.0/24 dev eth1 proto kernel scope link src 100.1.4.1
100.2.0.0/30 dev eth0 proto kernel scope link src 100.2.0.1

## Slide 45: starting the routing daemons
on each router (but r5) issue the following command:
root@r4:~$ systemctl start frr

## Slide 46: checking connectivity (again)
towards a remote destination
after a while, all remote destinations are reachable
root@r4:~$ ping 100.1.2.1
PING 100.1.2.1 (100.1.2.1) 56(84) bytes of data.
64 bytes from 100.1.2.1: icmp_seq=1 ttl=63 time=0.743 ms
64 bytes from 100.1.2.1: icmp_seq=2 ttl=63 time=0.875 ms
64 bytes from 100.1.2.1: icmp_seq=3 ttl=63 time=0.685 ms
--- 100.1.2.1 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2005ms
rtt min/avg/max/mdev = 0.685/0.767/0.875/0.085 ms

## Slide 47: checking the routing table
the routing table is now updated
root@r4:~$ ip route
100.1.0.0/30 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.0.4/30 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.0.8/30 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.0.12/30 dev eth3 proto kernel scope link src 100.1.0.14
100.1.0.16/30 dev eth2 proto kernel scope link src 100.1.0.18
100.1.1.0/24 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.2.0/24 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.3.0/24 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.4.0/24 dev eth1 proto kernel scope link src 100.1.4.1
100.2.0.0/30 dev eth0 proto kernel scope link src 100.2.0.1

## Slide 48: a look at ripv2 packets
root@r4:~$ tcpdump –tenni eth2 -v
let’s sniff ripv2 packets
display packet details
(enable full protocol decoding)

## Slide 49: a look at ripv2 packets
root@r4:~$ tcpdump –tenni eth2 –v
76:b9:c2:6b:d7:d8 > 01:00:5e:00:00:09, ethertype IPv4 (0x0800), length 166: (tos 0xc0, ttl 1, id 62062, offset 0, flags [DF], proto UDP (17), length 152)
100.1.0.17.520 > 224.0.0.9.520:
RIPv2, Response, length: 124, routes: 6 or less
AFI IPv4, 100.1.0.0/30, tag 0x0000, metric: 2, next-hop: self
AFI IPv4, 100.1.0.4/30, tag 0x0000, metric: 1, next-hop: self
AFI IPv4, 100.1.0.8/30, tag 0x0000, metric: 1, next-hop: self
AFI IPv4, 100.1.1.0/24, tag 0x0000, metric: 2, next-hop: self
AFI IPv4, 100.1.2.0/24, tag 0x0000, metric: 2, next-hop: self
AFI IPv4, 100.1.3.0/24, tag 0x0000, metric: 1, next-hop: self
let’s sniff ripv2 packets

## Slide 50: inspecting the rip routing table
kathara – [ lab: rip ]
root@r4:~$ vtysh
r4# show ip rip
Codes: R - RIP, C - connected, S - Static, O - OSPF, B - BGP
Sub-codes:
(n) - normal, (s) - static, (d) - default, (r) - redistribute,
(i) - interface
Network Next Hop Metric From Tag Time
R(n) 100.1.0.0/30 100.1.0.13 2 100.1.0.13 0 02:55
R(n) 100.1.0.4/30 100.1.0.17 2 100.1.0.17 0 02:27
R(n) 100.1.0.8/30 100.1.0.17 2 100.1.0.17 0 02:27
C(i) 100.1.0.12/30 0.0.0.0 1 self 0
C(i) 100.1.0.16/30 0.0.0.0 1 self 0
R(n) 100.1.1.0/24 100.1.0.13 2 100.1.0.13 0 02:55
R(n) 100.1.2.0/24 100.1.0.13 3 100.1.0.13 0 02:55
R(n) 100.1.3.0/24 100.1.0.17 2 100.1.0.17 0 02:27
C(r) 100.1.4.0/24 0.0.0.0 1 self 0
C(r) 100.2.0.0/30 0.0.0.0 1 self 0

## Slide 51: static routing
our network is a stub network (i.e., it has just one connection to an external router, r5); hence, static routes are enough for connecting it to the internet
r4
r1
r3
r2
inbound traffic
(to 100.1.0.0/16)
r5
outbound traffic
(to 0.0.0.0/0)

## Slide 52: adding a static route to r5
root@r5:~$ ip route add 100.1.0.0/16 via 100.2.0.1
root@r5:~$ ping 100.1.2.1
PING 100.1.2.1 (100.1.2.1) 56(84) bytes of data.
64 bytes from 100.1.2.1: icmp_seq=1 ttl=62 time=24.1 ms
64 bytes from 100.1.2.1: icmp_seq=2 ttl=62 time=1.11 ms
--- 100.1.2.1 ping statistics ---
2 packets transmitted, 2 received, 0% packet loss, time 1023ms
rtt min/avg/max/mdev = 1.117/12.634/24.151/11.517 ms

## Slide 53: configuring r4
step 1: configuring the default route
root@r4:~$ ip route add default via 100.2.0.2
root@r4:~$ ip route
default via 100.2.0.2 dev eth0
100.1.0.0/30 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.0.4/30 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.0.8/30 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.0.12/30 dev eth3 proto kernel scope link src 100.1.0.14
100.1.0.16/30 dev eth2 proto kernel scope link src 100.1.0.18
100.1.1.0/24 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.2.0/24 nhid 12 via 100.1.0.13 dev eth3 proto rip metric 20
100.1.3.0/24 nhid 10 via 100.1.0.17 dev eth2 proto rip metric 20
100.1.4.0/24 dev eth1 proto kernel scope link src 100.1.4.1
100.2.0.0/30 dev eth0 proto kernel scope link src 100.2.0.1

## Slide 54: configuring r4
root@r4:~$ vtysh
Hello, this is FRRouting (version 8.0.1).
Copyright 1996-2005 Kunihiro Ishiguro, et al.
r4# configure
r4(config)# router rip
r4(config-router)# route 0.0.0.0/0
r4(config-router)# quit
r4(config)# quit
r4# exit
step 2: propagating the default route into rip
begin configuration
configure the rip protocol
statically configure the default route
end of rip configuration
end configuration

## Slide 55: the default route
root@r1:~$ ip route
default nhid 12 via 100.1.0.14 dev eth0 proto rip metric 20
100.1.0.0/30 dev eth2 proto kernel scope link src 100.1.0.1
100.1.0.4/30 nhid 11 via 100.1.0.10 dev eth1 proto rip metric 20
100.1.0.8/30 dev eth1 proto kernel scope link src 100.1.0.9
100.1.0.12/30 dev eth0 proto kernel scope link src 100.1.0.13
100.1.0.16/30 nhid 12 via 100.1.0.14 dev eth0 proto rip metric 20
100.1.1.0/24 dev eth3 proto kernel scope link src 100.1.1.1
100.1.2.0/24 nhid 14 via 100.1.0.2 dev eth2 proto rip metric 20
100.1.3.0/24 nhid 11 via 100.1.0.10 dev eth1 proto rip metric 20
100.1.4.0/24 nhid 12 via 100.1.0.14 dev eth0 proto rip metric 20
100.2.0.0/30 nhid 12 via 100.1.0.14 dev eth0 proto rip metric 20
after a while, the default route has been injected (via rip) into the network

## Slide 56: checking connectivity
r5
eth0
1
eth0
2
L
r4
eth3
14
r1
H
100.1.0.12/30
100.2.0.0/30
eth0
13
root@r1:~$ ping 193.204.161.1
PING 193.204.161.1 (193.204.161.1) 56(84) bytes of data.
From 100.2.0.2 icmp_seq=1 Destination Net Unreachable
From 100.2.0.2 icmp_seq=2 Destination Net Unreachable
--- 193.204.161.1 ping statistics ---
2 packets transmitted, 0 received, +2 errors, 100% packet loss, time 999ms
any (even non-existing) destination

## Slide 57: checking connectivity
r5 is actually receiving echo request packets
root@r5:~$ tcpdump –tenni eth0
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth0, link-type EN10MB (Ethernet), capture size 1518 bytes
11:38:43.822503 arp who-has 100.2.0.2 tell 100.2.0.1
11:38:43.824221 arp reply 100.2.0.2 is-at fe:fd:64:02:00:02
11:38:43.825890 IP 100.1.0.13 > 193.204.161.1: icmp 64: echo request seq 1
11:38:43.827139 IP 100.2.0.2 > 100.1.0.13: icmp 92: net 193.204.161.1 unreachable
11:38:44.841566 IP 100.1.0.13 > 193.204.161.1: icmp 64: echo request seq 2
11:38:44.841651 IP 100.2.0.2 > 100.1.0.13: icmp 92: net 193.204.161.1 unreachable
6 packets captured
6 packets received by filter
0 packets dropped by kernel

## Slide 58: shutting down an interface
kathara – [ lab: rip ]
r5
r4
eth1
9
eth1
10
r1
r3
r2
G
100.1.0.8/30
root@r1:~$ traceroute 100.1.0.10
traceroute to 100.1.0.10 (100.1.0.10), 64 hops max, 40 byte packets
1 100.1.0.10 (100.1.0.10) 24 ms 1 ms 1 ms
root@r1:~$ ip link set eth1 down

## Slide 59: shutting down an interface
kathara – [ lab: rip ]
r5
eth2
18
r4
eth3
14
eth1
9
eth2
1
eth1
10
r1
r3
H
100.1.0.12/30
r2
eth2
17
eth0
13
G
I
100.1.0.16/30
100.1.0.8/30
r1 attempts forwarding the packet using the default route
?
root@r1:~$ traceroute 100.1.0.10
traceroute to 100.1.0.10 (100.1.0.10), 64 hops max, 40 byte packets
1 100.1.0.14 (100.1.0.10) 1 ms 1 ms 1 ms
2 * * *
3 * * *

## Slide 60: shutting down an interface
kathara – [ lab: rip ]
r5
eth2
18
r4
eth3
14
eth1
9
eth2
1
eth1
10
r1
r3
H
100.1.0.12/30
r2
eth2
17
eth0
13
G
I
100.1.0.16/30
100.1.0.8/30
after a while, routing information has been updated
root@r1:~$ traceroute 100.1.0.10
traceroute to 100.1.0.10 (100.1.0.10), 64 hops max, 40 byte packets
1 100.1.0.14 (100.1.0.14) 1 ms 1 ms 1 ms
2 100.1.0.10 (100.1.0.10) 5 ms 2 ms 1 ms

## Slide 61: about redistribute connected
by default (i.e., without further configuration) RIP already propagates information about all directly connected subnets attached to RIP-speaking interfaces
redistribute connected forces RIP to propagate information about all connected subnets
the semantic of redistribute connected applies to all routing protocols
the default behavior does not
  some protocols (e.g., bgp) are lazier, and do not propagate anything unless explicitly told to do so

## Slide 62: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.