## Slide 1: The Transport Layer
Gianluca Rizzo, UNITO

## Slide 2
application
transport
network
link
physical
BitTorrent
TCP
UDP
IP
Ethernet
DNS
web
The transport layer is sandwiched between the application layer and the network layer.
Therefore, we will need to involve the application and network layers in our discussion.

## Slide 3: But wait…why do we need another layer?
network
link
physical
IP
Ethernet
Notes: WE HAVE LEARNED HOW TO MAKE TWO end systems communicate, exchange information as IP packets.
Can’t we have just applications which plug directly on the network layer?

## Slide 5: First problem: many applications in a same end system, and many processes for each application….
One app, N processes
Each process independently communicate with other processes over the Internet
And every host runs many apps…
when a packet arrives at a host, how to understand to whom it belongs??

## Slide 6: There are still many things which can go wrong….
Just to name a few:
Packets who do not arrive at destination (e.g., dropped at a queue at a router/switch)
Packet which arrive in the wrong order
Packets which arrive too fast for the host to be able to store them and pass them to the destination process
And then network might get congested, and
not work if too much traffic is sent by sources….

## Slide 7: Yeah, but I can still program my app to take care of all this!
Sure! (And if you really want to go that way, UDP is for you)
But do you want to reinvent the wheel every time you code a new app?
The Transport layer offers application programmers an API (a set of functions) for communications over the Internet

## Slide 8: The transport layer protocols are two: UDP and TCP
UDP (“User Datagram Protocol”)
The minimalist one, it delegates all problems it can to the application
TCP (“Transmission Control Protocol”)
Takes care of many network issues, so you don’t have to
Available in many, many variants (we will see two)

## Slide 9: Then, what are the functions of the transport layer?
Process-to-process communication
  We’ll see how it is implemented in UDP and TCP
Reliable data delivery: Offering to the application layer the illusion of a reliable network
  First, the base mechanisms, on an imaginary protocol
  And then, their implementations in UDP and TCP
Notes: The first one (process-to-process communication) has to do with the fact that the transport layer is right below the application layer (where the various processes run). Hence, the transport layer is the one that first receives messages from processes and the one that finally delivers messages to processes.
The second one (reliable data delivery) is about offering to the application layer the illusion of a reliable network. The Internet is actually not reliable — packets may get corrupted or lost. However, the transport layer can try to recover from corruption and loss such that the application does not know that they happened.

## Slide 10: Who invented them?
TCP came first (1974) by Vint Cerf and Bob Kahn
They wrote a Request For Comments (RFC) and posted it for getting feedback at the Internet Engineering Task Force (IETF)
  IETF: The place where ideas and proposals about protocols are discussed and accepted as standards
  See RFC N.675 if you are curious

## Slide 11: Process-to-process communications

## Slide 12
App-layer message
Other transport-layer header fields
Source port #
Dest. port #
Other network-layer header fields
Source IP address
Dest. IP address
Network-layer header
Transport-layer header
segment
datagram
Structure of a typical Layer 3 packet
Notes: Let’s look at the structure of a typical Internet packet.
You have gotten a sense of this structure through the labs and the Wireshark took, but let’s look at it more carefully now.
First a process creates a message,
then the transport layer adds a transport-layer header,
and then the network layer adds a network-layer header.
Of the various header fields that the transport and network layer add,
today we will focus on the source and destination IP addresses and the source and destination port numbers.
These fields together specify a packet’s source and destination end-systems and processes.
Let’s also introduce two new terms:
A “segment” is the part of a packet that includes the app-layer message and the transport-layer header.
A “datagram” is the part of a packet that includes the app-layer message, the transport-layer header, and the network-layer header.
So, a packet typically includes a datagram, which typically includes a segment.

## Slide 13: What are the main steps of process-to-process communication with UDP?

## Slide 14: First, a definition…
What is a socket?
A data structure that lives in the transport layer and is associated with a particular local process.
It stores all the info about that process required by TCP or UDP to perform their functions

## Slide 15
Process S
application layer
transport layer
socket = new socket (UDP type)
socket.bind (IP address: 1.1.1.1, port: 1000)
for process S
IP address: 1.1.1.1
port: 1000
UDP socket
socket.sendto (message, dest. IP address: 5.5.5.5,
dest. port: 5000)
message
Source port: 1000
Dest. port: 5000
Source IP address: 1.1.1.1
Dest. IP address: 5.5.5.5
socket.close ( )
Notes: Suppose a process S wants to use UDP as its transport-layer protocol to send a message to a remote process:
First, the process asks the transport layer to open a UDP socket. In response, the transport layer creates a UDP socket and associates it with this process.
Second, the process asks the transport layer to bind the socket to a particular (local) IP address and port number. In response, the transport layer adds this information to the socket.
At this point, the process is ready to send a message through this socket. To do this, it calls a function and provides as arguments a pointer or reference to the message, the destination IP address, and the destination port number. In response, the transport layer starts putting together a packet: the message that the process is sending, the destination IP address and port number that the process passed as arguments through the sendto function, and the source IP address and port number that are associated with this socket.
  To be precise, the transport layer creates only the transport-layer header (which contains the source and destination port numbers, not the source and destination IP addresses), but it still keeps track of the source and destination IP addresses, because it needs to provide them to the network layer, which will create the network-layer header.
If the process does not need the socket any more, it asks the transport layer to close it. In response, the transport layer deletes the socket.

## Slide 16
Process R
socket = new socket (UDP type)
socket.bind (IP address: 5.5.5.5, port: 5000)
for process R
IP address: 5.5.5.5
port: 5000
UDP socket
message = socket.recvfrom (100 bytes)
message
Source port: 1000
Dest. port: 5000
Source IP address: 1.1.1.1
Dest. IP address: 5.5.5.5
socket.close ( )
application layer
transport layer
Notes: Now consider the receiving end: A process R wants to use UDP to receive a message from a remote process:
First, the process asks the transport layer to open a UDP socket. In response, the transport layer creates a UDP socket and associates it with this process.
Second, the process asks the transport layer to bind the socket to a particular (local) IP address and port number. In response, the transport layer adds this information to the socket.
At this point, the process is ready to receive a message through this socket. To do this, it calls a function and provides as argument the number of bytes that it wants to receive.
If a packet arrives from the network layer, the transport layer reads the headers and identifies which of the many processes that are running in the local application layer this packet is meant for. In this particular example, the transport layer will read from the packet’s headers that the destination IP address is 5.5.5.5 and the destination port number is 5000. Then it will ask: “Do I have a socket with this IP address and port number? Yes, I do, for process R”, so it will pass 100 bytes from the message to this process.
If the process does not need the socket any more, it asks the transport layer to close it. In response, the transport layer deletes the socket.

## Slide 17: UDP sockets
Each UDP socket has a unique (IP address, port #) -tuple
  Who makes sure this is unique?
A process may use the same UDP socket to communicate with many remote processes
Now let us look at TCP…

## Slide 18
Process S
socket = new socket (TCP type)
socket.bind (IP address: 1.1.1.1, port: 1000)
for process S
IP address:1.1.1.1
port:1000
TCP socket
socket.send (message)
message
Source port: 1000
Dest. port: 5000
Source IP address: 1.1.1.1
Dest. IP address: 5.5.5.5
socket.close ( )
socket.connect (rem. IP address: 5.5.5.5, rem. port: 5000)
rem. IP address:5.5.5.5
rem. port:5000
application layer
transport layer
Notes: Now suppose a process S wants to use TCP as its transport-layer protocol to send a message to another process.
The first two steps are similar to the UDP scenario:
First, the process asks the transport layer to open a TCP socket. In response, the transport layer creates a TCP socket and associates it with this process.
Second, the process asks the transport layer to bind the socket to a particular (local) IP address and port number. In response, the transport layer adds this information to the socket.
The next steps differ. Unlike UDP, a TCP sender establishes a connection to a TCP receiver:
The process asks the transport layer to connect the socket to a particular remote IP address and port number. In response, the transport layer adds this information to the socket and sends a TCP connection setup packet to the remote process.
If the connect function returns successfully, the process is ready to send a message through this socket. For this, it calls a function called “send” and provides as argument a pointer or reference to the message. In response, the transport layer starts putting together a packet with all the necessary information, including source and destination IP addresses and port numbers.
  Unlike with UDP, the process does not provide the destination IP address and destination port number as arguments to the send function, because the socket is already connected to a specific remote IP address and port number.
If the process does not need the socket any more, it asks the transport layer to close it. In response, the transport layer deletes the socket.

## Slide 19
Process R
socket = new socket (TCP type)
socket.bind (IP address: 5.5.5.5, port: 5000)
for process R
IP address:5.5.5.5
port:5000
TCP socket
connection-setup request
Source port: 1000
Dest. port: 5000
Source IP address: 1.1.1.1
Dest. IP address: 5.5.5.5
connSocket = socket.accept ( )
socket.listen (for N connections)
listening for N conn.
application layer
transport layer
Notes: Now consider the receiving end: A process R wants to use TCP to receive a message from another process:
Again, the first two steps are similar to the UDP scenario:
First, the process asks the transport layer to open a TCP socket. In response, the transport layer creates a TCP socket and associates it with this process.
Second, the process asks the transport layer to bind the socket to a particular (local) IP address and port number. In response, the transport layer adds this information to the socket.
The next steps differs:
The process tells the transport layer that it wants to use this socket to listen for TCP connection-setup requests from remote processes.
When a new TCP connection-setup request arrives, the transport layer reads the destination IP address and destination port number and sees that there exists a TCP socket listening for TCP connection-setup requests at this IP address and port number. Hence, it passes the request to process R.
If the process chooses to accept the request, it says so to the transport layer. In response, the transport layer…

## Slide 20
Process R
for process R
IP address:5.5.5.5
port:5000
TCP socket
message = connSocket.recv (100 bytes)
message
Source port: 1000
Dest. port: 5000
Source IP address: 1.1.1.1
Dest. IP address: 5.5.5.5
connSocket.close ( )
rem. IP address:1.1.1.1
rem. port:1000
application layer
transport layer
socket = new socket (TCP type)
socket.bind (IP address: 5.5.5.5, port: 5000)
connSocket = socket.accept ( )
socket.listen (for N connections)
Notes: …creates a new TCP “connection socket,” which is connected to the specific remote IP address and port number.
At this point, the process is ready to receive a message through this socket. For this, it calls a function called “recv” and provides as argument the number of bytes that it wants to receive.
If a packet arrives from the network layer, the transport layer reads the headers and identifies which of all the processes running at the local application layer this packet is meant for. In this particular example, the transport layer will read from the packet’s headers that the source IP address is 1.1.1.1, the destination IP address is 5.5.5.5, the source port number is 1000, and the destination port number is 5000. Then it will ask: “Do I have a socket with these IP addresses and port numbers? Yes, I do, for process R”, so it will pass 100 bytes from the message to this process.
If the process does not need the socket any more, it asks the transport layer to close it. In response, the transport layer deletes the socket.

## Slide 21: TCP sockets
Listening & connection sockets
Each connection socket has a unique (local IP, local port, remote IP, remote port) tuple
A process must use a different TCP connection socket per remote process

## Slide 22: The Transport layer implements process-to-process communication via connection multiplexing/demultiplexing
Multiplexing
  upon receiving a new message from a process, create new packets
  identify the correct IP addresses and ports
Demultiplexing
  many processes running in app layer
  upon receiving a new packet from the network, identify the correct dest. process
Notes: So, this is how the transport layer provides process-to-process communication:
At the sender side, we have “multiplexing”: the transport layer receives messages from many processes, through many sockets, and it “multiplexes” them, i.e, encapsulates them into segments which are sent over the same network.
At the receiver side, we have “demultiplexing”: upon receiving a segment from the network layer, the transport layer identifies the correct destination process, decapsulates the enclosed message, and passes it up.

## Slide 23: Reliable data delivery service at the Transport Layer
How can we build a transport layer that provides reliable data transfer on top of an unreliable network?
First, an imaginary protocol (neither TCP nor UDP)
  Examine the fundamental issues related to reliable data delivery, and some mechanisms to tackle them
Then, TCP and UDP
  That is, we will look into what is actually implemented
Notes: Now let’s turn to reliable data delivery.
We will first build our own imaginary protocol for reliable data delivery, which does not correspond to any actual transport-layer technology (it’s neither UDP nor TCP), and we will examine UDP and TCP in the next lecture.

## Slide 24
network
transport
transport
app
app
network
Alice’s computer
Bob’s computer
Notes: In this pictures, I have rotated the layers by 90 degrees, so that I can depict two end-systems, a sender and a receiver.
On the left we have Alice’s app layer, which talks to Alice’s transport layer, which talks to the network, which talks to Bob’s transport layer, which talks to Bob’s app layer.
The network layer of the Internet is unreliable: it may corrupt or drop packets.
Let’s see how we can build a transport layer that provides reliable data transfer on top of an unreliable network. I.e., we want a transport layer that provides to the application layer the illusion of a reliable network.

## Slide 25
rdt_send()
udt_send()
rdt_rcv()
deliver_data()
Alice’s computer
Bob’s computer
Notes: Consider Alice’s and Bob’s computers. Suppose a process in Alice’s application layer wants to send a message to a process in Bob’s application layer.
Suppose the message fits in a single segment.
Here is the minimum that happens:
Alice’s app layer calls a function, called rdt_send (reliable-data-transfer_send), to pass the message to the transport layer.
Alice’s transport layer calls another function, called udt_send (unreliable-data-transfer_send), to pass the segment to the network layer.
The segment traverses the network from Alice to Bob.
Bob’s network layer calls rdt_rcv (reliable-data-transfer_receive) to pass the segment to the transport layer.
And the transport layer calls deliver_data to pass the message to the app layer.
This transport layer that I just described does nothing but pass data between the application and network layers. It does nothing useful, it might as well not be there.
Now let’s start adding useful functionality.
First, the transport layer can detect that a segment was corrupted.
This can be done by using a…

## Slide 26: Checksum
Redundant information
  e.g., the binary sum of all data bytes
Sender adds checksum C to each segment
  transport-layer header field
Receiver uses it to detect data corruption
  receiver recomputes checksum C’
  if C’!= C, segment was corrupted
Notes: ... checksum,
which is redundant information that depends on the data,
e.g., the sum of all the data bytes.
The sender adds a checksum to each segment.
The receiver recomputes the checksum and determines whether the segment was corrupted or not.
Certain checksums make it possible to not only detect corruption but also correct limited forms of corruption, but we will not discuss this scenario today.

## Slide 27
Alice’s computer
Bob’s computer
rdt_send()
udt_send()
rdt_rcv()
deliver_data()
NACK
udt_send()
udt_send()
rdt_rcv()
rdt_rcv()
udt_send()
ACK
rdt_rcv()
Notes: Suppose that Alice sends a segment to Bob, and Bob’s transport layer determines (using the checksum) that the segment was corrupted.
What can it do next?
It can send back to Alice’s transport layer a negative ACK (NACK).
In response, Alice’s transport layer retransmits the same segment.
If the retransmitted segment arrives at its destination uncorrupted, Bob’s transport layer extracts the data, delivers it to the application layer, and sends back a positive ACK.

## Slide 28: Acknowledgment + retransmission
Feedback from receiver to sender
Receiver adds ACK to each segment
  transport-layer header field
Sender uses it to detect and overcome data corruption
  if sender gets negative ACK, it retransmits the data
  Problem: Ack segments can be corrupted too!
Notes: So: An important element of reliable data delivery is the combination of acknowledgments (ACKs) and retransmissions…

## Slide 29
Alice’s computer
Bob’s computer
rdt_send()
udt_send()
rdt_rcv()
deliver_data()
?AC?
udt_send()
udt_send()
rdt_rcv()
rdt_rcv()
udt_send()
ACK 0
rdt_rcv()
SEQ 0
SEQ 0
Notes: Suppose that Alice sends a segment to Bob, and Bob’s transport layer sends back a positive ACK. However, the ACK gets corrupted, and Alice’s transport layer cannot tell if it’s a positive or a negative ACK. What must Alice’s transport layer do?
It must be conservative and retransmit the segment.
However, Bob’s transport layer (which has already successfully received this segment) may now think that Alice’s transport layer is transmitting a new segment, whereas she is *re*transmitting the old one.
To resolve this issue, we need sequence numbers:
- When Alice’s transport layer sends a segment, it adds a sequence number to it.
- If it retransmits the same segment, that segment has the same sequence number,
so Bob knows that Alice is retransmitting the same segment.

## Slide 30
Alice’s computer
Bob’s computer
rdt_send()
udt_send()
rdt_rcv()
deliver_data()
ACK 0
udt_send()
udt_send()
rdt_rcv()
rdt_rcv()
udt_send()
ACK 1
rdt_rcv()
SEQ 0
SEQ 1
deliver_data()
Notes: - If Alice’s transport layer transmits a new segment, that has a different sequence number,
so Bob’s transport layer knows that Alice is transmitting a new segment.
-> How many sequence numbers do we need?

## Slide 31: Sequence number
An identifier for data
Sender adds SEQ to each segment
  transport-layer header field
Receiver uses it to disambiguate data
Sequence numbers make it possible to have *implicit* negative ACKs
Notes: So: Another important element of reliable data delivery is sequence numbers…

## Slide 32
Alice’s computer
Bob’s computer
rdt_send()
udt_send()
rdt_rcv()
deliver_data()
ACK 0
udt_send()
udt_send()
rdt_rcv()
rdt_rcv()
udt_send()
NACK 1
rdt_rcv()
SEQ 0
SEQ 1
Notes: For example, suppose Bob’s transport layer needs to send a NACK for segment 1.
Instead…

## Slide 33
Alice’s computer
Bob’s computer
rdt_send()
udt_send()
rdt_rcv()
deliver_data()
ACK 0
udt_send()
udt_send()
rdt_rcv()
rdt_rcv()
udt_send()
ACK 0
rdt_rcv()
SEQ 0
SEQ 1
Notes: it can send a (second) ACK for segment 0, which means: “The last segment I received correctly from you had SEQ 0.” This is equivalent with Bob sending a NACK for segment 1.

## Slide 34
Alice’s computer
Bob’s computer
rdt_send()
udt_send()
rdt_rcv()
udt_send()
udt_send()
ACK 0
rdt_rcv()
SEQ 0
SEQ 0
deliver_data()
X
timeout
Notes: Now suppose Alice sends a segment to Bob, and the segment is lost.
Now Alice’s transport layer receives no feedback at all about its segment.
To deal with this scenario, Alice’s transport layer uses timeouts:
- Every time it transmits a segment, it starts a timer.
- If the timer expires and Alice’s transport layer has not received an ACK for the segment,
it assumes the segment lost and retransmits.

## Slide 35
Alice’s computer
Bob’s computer
rdt_send()
udt_send()
rdt_rcv()
udt_send()
udt_send()
ACK 0
rdt_rcv()
SEQ 0
deliver_data()
X
timeout
deliver_data()
udt_send()
rdt_rcv()
SEQ 0
ACK 0
Notes: What if Alice’s segment reaches Bob, but Bob’s ACK is lost?
Alice’s transport layer still times out and retransmits the segment.
In general, there is no way for Alice’s transport layer to know if a timeout is due to a segment really being lost or the ACK for the segment being lost. It must act conservatively and retransmit anyway.

## Slide 36
Alice’s computer
Bob’s computer
rdt_send()
udt_send()
rdt_rcv()
udt_send()
SEQ 0
timeout
deliver_data()
udt_send()
rdt_rcv()
SEQ 0
ACK 0
rdt_rcv()
rdt_rcv()
udt_send()
SEQ 1
deliver_data()
udt_send()
rdt_rcv()
Notes: And what if Alice’s segment reaches Bob, and Bob’s ACK reaches Alice, but (due to some unpredicted network delay) after Alice’s transport layer has timed out?
There’s no way for Alice’s transport layer to avoid useless retransmissions like this one. However, when Alice’s transport layer receives the first (the delayed) ACK 0, it can immediately transmit SEQ 1 — it does not need to wait for Bob’s second ACK 0.
In the meantime, when Bob’s transport layer receives the retransmitted SEQ 0,
it will ACK 0 again, and that’s OK. Alice’s transport layer will just ignore the second ACK 0.

## Slide 37: Timers and timeouts
No arrival of an expected ACK
  a segment was lost or delayed
  the ACK for a segment was lost or delayed
Sender uses it to overcome data loss
  if the sender times out, it retransmits
Notes: So: Yet another important element of reliable data delivery is the timeout…

## Slide 38: Basic elements
Checksums
  detect data corruption
ACKs + retransmissions + SEQs
  overcome data corruption
Timeouts + ACKs + retransmissions + SEQs
  overcome data loss

## Slide 39
ACK 0
SEQ 1
SEQ 0
ACK 1
transmission
RTT
transmission
RTT
Alice’s computer
Bob’s computer
Notes: I have described to you a “stop-and-wait” transport-layer protocol, where the sender always sends only one segment and then waits for an ACK or a timeout.
Here is what communication looks like when no segment is corrupted or lost.
—>What is the problem with this protocol?
Performance and, in particular, throughput.
Alice’s transport layer transmits one segment, then waits for an ACK.
Then she transmits another segment, then waits for an ACK.
And so on.

## Slide 40
transmission rate R=1 Gbps
packet size L = 1000 b
Alice’s computer
Bob’s computer
transmission delay = L/R = 8 us
propagation delay = 15 ms
Notes: Let’s go back, for a moment, to this view of sender and receiver.
Suppose Alice’s and Bob’s computers are directly connected over one physical link of transmission rate 1 Gbps and propagation delay 15 msec.
Suppose the segment size is 1000 bytes.
Hence, the transmission delay for each segment is 8 usec.

## Slide 41
0.008 ms
30 ms
Busy for
0.008
30.008
= 0.00027
sender/channel utilization
Alice’s computer
Bob’s computer
ACK 0
SEQ 0
Notes: This means that Alice transmits for 8 usec and then does nothing for 30 msec.
This is a long wait.
Another way to put this is that Alice’s transport layer is busy only for 0.027% of the time.
We call this number the *sender* or *channel utilization*.
So, the stop-and-wait protocol has poor sender utilization.
—>How can we improve sender utilization?

## Slide 42
Alice’s computer
Bob’s computer
ACK 0
SEQ 0
SEQ 1
SEQ 2
SEQ 3
ACK 1
ACK 2
ACK 3
0
1
2
3
4
5
6
7
window size N = 4
SEQ 4
SEQ 5
SEQ 6
SEQ 7
Notes: Let’s introduce the notion of a sender window.
What I am showing here on the left are sequence numbers that Alice will use,
and this rectangle indicates that she has a window of size 4,
which means that she will send out up to 4 segments without waiting for an ACK.
For example:
- She sends out segments 0 to 3, then stops.
- When she receives Bob’s first ACK, she advances her window by 1 SEQ, which means that she can send out segment 4.
- When she receives Bob’s second ACK, she advances her window by 1 more SEQ,
which means that she can send out segment 5.
- And so on.
At any point in time, she has sent no more than 4 unacknowledged segments.
We say that her window size is 4.

## Slide 43
transmission
RTT
Busy for
trans. N
trans. + RTT
Alice’s computer
Bob’s computer
SEQ 0
SEQ 1
SEQ 2
SEQ 3
ACK 0
Notes: Let’s see by how much we have improved sender utilization:
Now Alice transmits 4 segments and waits for an ACK,
so, she is busy for transmission delay times 4,
divided by transmission delay + RTT.
So, we have improved sender utilization by a factor N,
which is the sender’s window size — in our specific example, 4.
—>How large would you make N?
—>Is there any reason to not increase N arbitrarily?

## Slide 44: Improving sender utilization through Pipelining
Stop and wait: poor sender utilization
  the sender does nothing while waiting for the receiver’s ACK or the timeout
Pipelining: better utilization
  the sender sends up to N un-ACKed segments
  N = sliding window size
Notes: We first put together what we call a “stop and wait” protocol:
The sender sends out a segment, then does nothing until it receives an ACK from the receiver, or it times out.
Then we put together what we call a “pipelined” protocol,
where the sender sends out multiple unacknowledged segments.
The advantage of pipelining is that it improves sender utilisation by a factor that is equal to the sender’s window size.
—
But what happens when we use pipelining and segments get corrupted or lost?
There are two protocols that address this scenario:

## Slide 45: What happens in Pipelining when a segment gets corrupted/lost?
Two strategies to deal with this:
Go-back-N
Selective Repeat
Notes: We first put together what we call a “stop and wait” protocol:
The sender sends out a segment, then does nothing until it receives an ACK from the receiver, or it times out.
Then we put together what we call a “pipelined” protocol,
where the sender sends out multiple unacknowledged segments.
The advantage of pipelining is that it improves sender utilisation by a factor that is equal to the sender’s window size.
—

## Slide 46
ACK 0
SEQ 1
SEQ 2
SEQ 3
ACK 1
X
timeout for packet 2
0
1
2
3
4
5
6
7
SEQ 0
SEQ 4
SEQ 5
ACK 1
0
1
2
3
4
5
6
7
0
1
X
X
X
Alice’s computer
Bob’s computer
Notes: The first one is called Go-back-N:
The receiver never accepts any out-of-order segments:
- The receiver also has a window, of size 1.
- This means that the receiver is willing to accept only one SEQ.
- It discards anything else.
For example:
- Alice sends segment 0, Bob receives it, and advances his window by 1 SEQ, which means that he is now ready to receive segment 1.
- Alice sends segment 1, and now Bob is ready to receive segment 2.
- Alice sends segment 2, but it is dropped.
- When she sends segment 3, Bob discards it, because his window is stuck at 2.
In the meantime, Bob has ACKed segment 0.
When Alice receives ACK 0, she advances her window by 1 SEQ, and sends segment 4, but Bob rejects it, because his window is still stuck at 2.
Bob has also ACKed segment 1.
When Alice receives ACK 1, she again advances her window by 1 SEQ, and sends segment 5, but Bob rejects it.
When Bob receives segment 3, he still ACKs segment 1, indicating that that is the last segment that he received in order.
When does Alice realize that something is wrong?
When she times out waiting for an ACK for segment 2.

## Slide 47
ACK 2
SEQ 2
SEQ 4
ACK 3
SEQ 5
0
1
2
3
4
5
6
7
SEQ 3
ACK 4
0
1
2
3
4
5
6
7
0
1
Alice’s computer
Bob’s computer
ACK 5
2
3
4
5
Notes: At that point, she retransmits segment 2 plus all the subsequent segments that she has sent out, because she knows that Bob must have discarded them, since he did not receive her original segment 2. Once Bob has received all the retransmitted segments correctly and ACKed them, Alice can advance her window and move on.
In this approach, when Bob ACKs segment 1, that means that he has correctly received every segment up to and including 1. This is called a **cumulative ACK**.

## Slide 48: Main features of Go-back-N
The receiver accepts no out-of-order segments
ACKs are cumulative
  an ACK for segment 10 indicates that all segments until and including 10 have been received
When the sender retransmits, it retransmits all the un-ACK-ed segments

## Slide 49
X
timeout for packet 2
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
0
1
3
4
5
3
Alice’s computer
Bob’s computer
SEQ 1
SEQ 2
SEQ 3
SEQ 0
ACK 0
ACK 1
ACK 3
SEQ 4
SEQ 5
ACK 4
ACK 5
4
5
Notes: The other pipelining protocol is called Selective Repeat:
The receiver does accept a certain number of out-of-order segments:
- The receiver has a window, same size as the sender’s (in our example 4),
- which means that the receiver is willing to accept up to 4 out-of-order segments.
For example:
When segment 0 arrives, Bob advances his window by 1 SEQ.
Same when segment 1 arrives.
Segment 2 is dropped.
When segment 3 arrives, Bob does not discard it, because SEQ 3 is inside his window, so he accepts and ACKs segment 3.
In the meantime, Bob has ACKed segment 0, causing Alice to advance her window by 1 SEQ and send out a new segment.
Same when Bob ACKs segment 1.
When Bob ACKs segment 3, Alice does not transmit a new segment, because her window is now closed.
Same when Bob ACKs segments 4 and 5.
Alice realizes that something is wrong when she times out waiting for an ACK for segment 2.

## Slide 50
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
0
1
3
4
5
3
2
Alice’s computer
Bob’s computer
SEQ 2
ACK 2
2
4
5
Notes: At that point, she retransmits only segment 2. When Bob receives the retransmitted segment, he can finally advance his window and ACK 2. When Alice receives ACK 2, she also advances her window.
In this approach, when Bob ACKs segment 1, that means that he has correctly segment 1, it does not say anything about previous segments. This is called a **selective ACK**.

## Slide 51: Selective Repeat
The receiver accepts N-1 out-of-order segments
ACKs are selective
  an ACK for segment 10 indicates that segment 10 has been received
When the sender retransmits, it retransmits only one segment

## Slide 52: Question
When would you prefer a GoBackN protocol, and when would you prefer a Selective Repeat protocol?