## Slide 1: Laboratory: OSPF multiarea

## Slide 2: What are OSPF areas?
An abstraction that simplifies administration and improves scalability
  the topology of an area is invisible from the outside
  routers internal to a given area don’t see the detailed external topology
Each area runs a separate instance of the link state routing algorithm
  all routers in an area construct the same lsdb
  each router keeps a distinct lsdb for each area it belongs to

## Slide 3: OSPF areas
They are identified by a 32-bit number, often in dotted decimal notation (1.2.3.4)
  different interfaces of the same router can be assigned to different areas
  each
    router interface...
    network...
    router adjacency...
  ...is associated with a single area

## Slide 4: Area types
backbone (0.0.0.0)
  must be (virtually) connected
  all other areas are connected to it
  contains all the area border routers
stub
  It does not receive advertisements of external routes (?)
  internal nodes are offered a default route
  cannot contain autonomous system boundary routers
  the backbone can’t be a stub area
transit
  used to pass traffic from one adjacent area to another, via virtual links

## Slide 5
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
backbone
stub
stub
stub

## Slide 6: Router types
internal router
  all interfaces belong to the same area
area border router (abr)
  connects one or more areas to the backbone
  keeps multiple lsdbs, one for each area
backbone router
  has at least one interface connected to the backbone
  an abr is always a backbone router
autonomous system boundary router (asbr)
  imports and floods routing information from other routing protocols (typically, bgp)
note: a router can be of more than one type

## Slide 7
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1

## Slide 8
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1
backbone
routers

## Slide 9
kathara – [ labs: ospf ]
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1
area border
routers

## Slide 10
kathara – [ labs: ospf ]
bb4
bb0
0.0.0.0
1.1.1.1
2.2.2.2
3.3.3.3
r1
r2
r6
bb3
r5
bb2
r4
r3
bb1
internal
routers

## Slide 11: Path Types
OSPF classifies routes into path types based on their origin and location relative to areas,
strict preference order for shortest path selection:
intra-area > inter-area > external type 1 (E1) > external type 2 (E2).

## Slide 12: Path types
Intra-Area (O)
    Routes to destinations within the same OSPF area, using the full link-state database for SPF calculation. Highest preference as they reflect local topology details.​
Inter-Area (O IA)
    Routes to other OSPF areas, learned via ABR summary LSAs (Type 3). Cost includes intra-area to ABR + backbone path + intra-area from destination ABR; visible as aggregated summaries.​

## Slide 13: Path types
External Type 1 (E1)
    Redistributed external routes (e.g., from BGP, static) where total cost = external metric + OSPF internal cost to ASBR.
    Preferred over E2; used when internal paths vary significantly.
External Type 2 (E2)
    Default for external routes; cost = external metric only (OSPF cost to ASBR as tie-breaker).
    Ideal when external costs dominate or ASBRs are equidistant.

## Slide 14: Example – Intra-Area path

## Slide 15
kathara – [ labs: ospf ]
10.0.3.0/24
10.0.1.0/24
bb4
10.0.2.0/24
10.0.0.0/24
bb0
eth0
3
eth1
3
D
A
B
C
0.0.0.0
eth0
2
eth2
1
E
100.0.0.0/30
1.1.1.1
2.2.2.2
3.3.3.3
r1
eth0
2
eth1
1
I
200.0.0.0/30
r2
J
200.0.1.0/24
r6
L
220.0.0.0/30
N
220.0.1.0/30
M
220.0.2.0/30
eth0
1
eth1
1
eth0
2
eth1
2
eth1
1
eth1
1
eth0
1
eth0
2
eth1
2
eth1
1
eth0
1
eth1
2
eth1
1
eth0
2
eth0
2
bb3
210.0.0.0/24
r5
eth2
2
eth2
1
H
130.0.0.0/30
bb2
eth3
1
r4
G
120.0.0.0/30
eth0
2
K
eth3
1
110.0.0.0/30
F
eth1
2
eth2
1
r3
bb1
90
100
default cost (10) is assumed where unspecified

## Slide 16: area configuration
area information is found in two places
  when enabling ospf on router interfaces network 200.0.0.0/16 area 1.1.1.1
  when specifying the area type (not required for the backbone) area 1.1.1.1 stub

## Slide 18: ospf path types
there are 4 path types
  intra-area
  inter-area
  external type 1
  external type 2
types can coexist in the same network
each type is preferred over the following ones

## Slide 19: ospf path types
intra-area paths
  calculated using the shortest-path tree

## Slide 20: ospf path types
inter-area paths
  abrs inject summary information inside each area, to make it aware of available destinations in other areas
    such information includes the cost of the shortest path from the abr to the destination
    if multiple subnets are summarized into a single network, the route cost will be the maximum cost to any of the component subnets
  an inter-area path is always composed of:
    an intra-area path from the source to the abr
    a backbone path between the source and destination areas
    an intra-area path to the destination

## Slide 21: ospf path types
external paths are learned from other routing protocols (e.g., bgp)
type 1: the cost is expressed in terms of
  the external (bgp) route cost* +
  the ospf cost to the asbr
  example with bgp cost=495, ospf cost=10: N E1 50.0.0.0/16 [505] tag: 0 via 10.0.1.2, eth1
* cost used when redistributing the protocol (bgp) into ospf; default for bgp=20; configurable by using redistribute bgp metric value

## Slide 22: ospf path types
type 2: the cost is expressed in terms of
  the external (bgp) route cost* only (distance to the asbr is only used to break ties)
  example with bgp cost=495, ospf cost=10: N E2 50.0.0.0/16 [10/495] tag: 0
  via 10.0.1.2, eth1
  metric type is user-configurable redistribute bgp metric-type 2 metric 495

## Slide 23: experiments
check that routers know detailed topology information only about their own area
r2# show ip ospf neighbor
Neighbor ID Pri State Up Time Dead Time Address Interface RXmtL RqstL DBsmL
200.0.0.1 1 Full/Backup 1m17s 32.279s 200.0.0.1 eth0:200.0.0.2 0 0 0
r2

## Slide 24: experiments
check that routers know detailed topology information only about their own area
r2# show ip ospf database router
OSPF Router with ID (200.0.1.1)
Router Link States (Area 1.1.1.1 [Stub])
...
Link State ID: 110.0.0.1
...
Number of Links: 1
Link connected to: a Transit Network
(Link ID) Designated Router address: 100.0.0.2
(Link Data) Router Interface address: 100.0.0.1
...
Link State ID: 200.0.0.1
...
Number of Links: 2
Link connected to: a Transit Network
(Link ID) Designated Router address: 100.0.0.2
(Link Data) Router Interface address: 100.0.0.2
...
Link connected to: a Transit Network
(Link ID) Designated Router address: 200.0.0.2
(Link Data) Router Interface address: 200.0.0.1
...
r2
note: the output has been summarized

## Slide 25: experiments
check that routers know detailed topology information only about their own area
r2# show ip ospf database network
OSPF Router with ID (200.0.1.1)
Net Link States (Area 1.1.1.1 [Stub])
LS age: 759
Options: 0x0 : *|-|-|-|-|-|-|-
LS Flags: 0x6
LS Type: network-LSA
Link State ID: 100.0.0.2 (address of Designated Router)
Advertising Router: 200.0.0.1
LS Seq Number: 80000001
Checksum: 0x09ec
Length: 32
Network Mask: /30
Attached Router: 110.0.0.1
Attached Router: 200.0.0.1
LS age: 763
Options: 0x0 : *|-|-|-|-|-|-|-
LS Flags: 0x3
LS Type: network-LSA
Link State ID: 200.0.0.2 (address of Designated Router)
Advertising Router: 200.0.1.1
LS Seq Number: 80000001
...
r2
note: the output has been summarized

## Slide 26: experiments
check what routers know about the outside of the area, using the show ip ospf database summary command
  in particular, check the Metric values, that show how far away the destination is from the advertising abr
check that routers in stub areas are offered a default route, whereas routers in the backbone are not
  also check what Metric is assigned to the default route

## Slide 27: experiments
r3# show ip ospf route
============ OSPF network routing table ============
N IA 0.0.0.0/0 [11] area: 2.2.2.2
via 110.0.0.1, eth1
via 120.0.0.1, eth0
...
r3
experiment ospf’s recovery capabilities
  when multiple equal cost routes are available, ospf keeps all of them
  check it by verifying what r3 knows about the default route
inter-area path
equal cost routes

## Slide 28: experiments
r3# show ip route
Codes: K - kernel route, C - connected, S - static, R - RIP, O - OSPF,
I - IS-IS, B - BGP, E - EIGRP, N - NHRP, T - Table, v - VNC,
V - VNC-Direct, A - Babel, F - PBR, f - OpenFabric, > - selected route,
* - FIB route, q - queued, r - rejected, b - backup t - trapped, o - offload failure
O>* 0.0.0.0/0 [110/11] via 110.0.0.1, eth1, weight 1, 00:18:15
* via 120.0.0.1, eth0, weight 1, 00:18:15
r3
experiment ospf’s recovery capabilities
  when multiple equal cost routes are available, ospf keeps all of them
  check it by verifying what r3 knows about the default route
  zebra performs the actual selection

## Slide 29: experiments
experiment ospf’s recovery capabilities
  when multiple equal cost routes are available, ospf keeps all of them
  check it by verifying what r3 knows about the default route
  zebra performs the actual selection
    now bring bb1’s eth3 down using ifconfig, wait a few seconds and check how the routing is changed
    bring bb1’s eth3 back up and check again how the routing is changed

## Slide 30: lab: ospf-complex

## Slide 31
last update: Nov 2018
kathara – [ labs: ospf ]
10.0.3.0/24
10.0.1.0/24
bb4
10.0.2.0/24
10.0.0.0/24
bb0
eth0
3
eth1
3
D
A
B
C
0.0.0.0
eth0
2
eth2
1
E
100.0.0.0/30
1.1.1.1
2.2.2.2
3.3.3.3
r1
eth0
2
eth1
1
I
200.0.0.0/30
r2
J
200.0.1.0/24
r6
L
220.0.0.0/30
N
220.0.1.0/30
M
220.0.2.0/30
eth0
1
eth1
1
eth0
2
eth1
2
eth1
1
eth1
1
eth0
1
eth0
2
eth1
2
eth1
1
eth0
1
eth1
2
eth1
1
eth0
2
eth0
2
bb3
as100r1
210.0.0.0/24
eth2
1
eth0
2
O
140.0.0.0/30
r5
50.0.0.0/16
AS10
AS100
eth2
2
eth2
1
H
130.0.0.0/30
bb2
eth3
1
r4
G
120.0.0.0/30
eth0
2
K
eth3
1
110.0.0.0/30
F
eth1
2
eth2
1
r3
bb1
90
100
default cost (10) is assumed where unspecified

## Slide 32: lab description
same as multiarea + some information is injected via bgp from an external as
  also, abrs are configured to just inject the default route area 1.1.1.1 stub no-summary
perform the same experiments as for the multiarea lab
  in addition, check asbr information using
    show ip ospf database asbr-summary
  also check that such information is not propagated inside stub areas

## Slide 33: A quick note about stub networks
“stub” = not used for transit
three possible situations:
kathara – [ labs: ospf ]
r2
J
200.0.1.0/24
eth1
1
ospf is enabled also on the stub network’s interface
the stub network is advertised in the entire ospf domain
interface uselessly sends hello packets
ospf is not enabled on the stub network’s interface
the stub network is advertised
the stub network is advertised as an AS-external route (hence, only through the backbone)
ospf is enabled on the stub network’s interface, which is configured as passive-interface
the stub network is advertised in the entire ospf domain
N/A
then
but
then
but
then
but